## Slide 1
3140707
Computer Organization & Architecture
Unit-1
Computer Data Representation & Register Transfer and Micro-operations

## Slide 2: Topics to be covered
Basic computer data types
Complements
Fixed point representation
Floating point representation
Register Transfer language
Register Transfer
Bus and Memory Transfers (Three-State Bus Buffers, Memory Transfer)
Arithmetic Micro-Operations
Logic Micro-Operations
Shift Micro-Operations
Arithmetic logical shift unit

## Slide 3: Basic Computer Data Types
Decimal Number System
  Radix(r) = 10, Number range = 0 - 9
Binary Number System
  Radix(r) = 2, Number range = 0 - 1
Octal Number System
  Radix(r) = 8, Number range = 0 - 7
Hexadecimal Number System
  Radix(r) = 16, Number range = 0 - 9 & A - F
Binary Coded Decimal Numbers

## Slide 4: Complements
(r-1)’s complement
  9’s complement
  1’s complement
  7’s complement
  15’s complement
r’s complement
  10’s complement
  2’s complement
  8’s complement
  16’s complement

## Slide 5: Fixed Point Representation
Integer Representation
  Signed-magnitude representation
  1’s complement representation
  2’s complement representation
Arithmetic Addition
  Using 1’s complement
  Using 2’s complement
Arithmetic Subtraction
  Using 1’s complement
  Using 2’s complement

## Slide 6: Floating Point Representation
Two parts
  Mantissa – Represents signed fixed-point number
  Exponent – Represents position of the decimal point
For example, the decimal number +6132.789 is represented in floating-point with a fraction and an exponent as follows:
Fraction
+0.6132789
Exponent
+04
The value of the exponent indicates that the actual position of the decimal point is four positions to the right of the indicated decimal point in the fraction.
Floating-point is always interpreted to represent a number in the following form: m X re
Here, m stands for mantissa, e stands for exponent, r means radix.

## Slide 7: Floating Point Representation
Normalization
  A floating point number is said to be normalized if the most significant digit of the mantissa is nonzero.
  For example, the decimal number 350 is normalized but 00035 is not.
ANSI 32-bit floating point byte format
Byte 1
SEEEEEEE
Byte 2
.MMMMMMMM
Byte 3
Byte 4
MMMMMMMM
MMMMMMMM
S = Sign of Mantissa, E = Exponent bits, M = Mantissa bits
Example, 13 = 1101 = 0.1101 x 24
= 00000100 .11010000 00000000 00000000
Example, -17 = - 10001 = -0.10001 x 25
= 10000101 .10001000 00000000 00000000

## Slide 8: Register Transfer Language
Unit – 1: Data Representation & RTL Darshan Institute of Engineering & Technology

## Slide 9: Register
Computer Registers are designated by capital letters.
For example,
  MAR – Memory Address Register
  PC – Program Counter
  IR – Instruction Register
  R1 – Processor Register
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0
15
PC (H) | PC (L)
0
7
8
15
Register R
Showing individual bits
Numbering of bits
Divided into two parts

## Slide 10: Microoperations
The operations executed on data stored in registers are called microoperations.
A microoperation is an elementary operation performed on the information stored in one or more registers.
The result of the operation may replace the previous binary information of a register or may be transferred to another register.
Example:
Shift, count, clear and load

## Slide 11: Register Transfer Language
The symbolic notation used to describe the microoperation transfers among registers is called a register transfer language.
The term "register transfer" implies the availability of hardware logic circuits that can perform a stated microoperation and transfer the result of the operation to the same or another register.
A register transfer language is a system for expressing in symbolic form the microoperation sequences among the registers of a digital module.

## Slide 12: Register Transfer
Information transfer from one register to another is designated in symbolic form by means of a replacement operator is known as Register Transfer.
The statement
denotes a transfer of the content of register into register .
1 | 1 | 0 | 1
1 | 1 | 0 | 1
R1
R2

## Slide 13: Register Transfer with Control Function
Normally, we want the transfer to occur only under a predetermined control condition using if-then statement.
If (P = 1) then ()
where P is a control signal generated in the control section.
A control function is a Boolean variable that is equal to 1 or 0. The control function is included in the statement as follows:
Control
circuit
Load
P
Clock
n
t
t+1
Transfer occurs here
Load

## Slide 14: Bus and Memory Transfers
Unit – 1: Data Representation & RTL Darshan Institute of Engineering & Technology

## Slide 15: Common Bus System for 4 registers
A typical digital computer has many registers, and paths must be provided to transfer information from one register to another.
The number of wires will be excessive if separate lines are used between each register and all other registers in the system.
3 2 1 0
3 2 1 0
3 2 1 0
Register A
Register B
Register C

## Slide 16: Common Bus System for 4 registers
A more efficient scheme for transferring information between registers in a multiple-register configuration is a common bus system.
A bus structure consists of a set of common lines, one for each bit of a register, through which binary information is transferred one at a time.
One way of constructing a common bus system is with multiplexers.
The multiplexers select the source register whose binary information is then placed on the bus.

## Slide 17: Common Bus System for 4 registers
4 x 1
MUX 3
3 2 1 0
3 2 1 0
4 x 1
MUX 2
3 2 1 0
3 2 1 0
4 x 1
MUX 1
3 2 1 0
3 2 1 0
4 x 1
MUX 0
3 2 1 0
3 2 1 0
S1
S0
4-line common bus
D2
D1
D0
C2
C1
C0
B2
B1
B0
A2
A1
A0
Register A
Register B
Register C
Register D
D2
D1
D0
C2
C1
C0
B2
B1
B0
A2
A1
A0
0
0
A2
A1
A0
A3

## Slide 18: Common Bus System for 4 registers
The construction of a bus system for four registers is explained earlier.
Each register has four bits, numbered 0 through 3.
The bus consists of four 4 x 1 multiplexers each having four data inputs, 0 through 3, and two selection inputs, S1 and S0.
The diagram shows that the bits in the same significant position in each register are connected to the data inputs of one multiplexer to form one line of the bus.

## Slide 19: Common Bus System for 4 registers
The two selection lines S1 and S0 are connected to the selection inputs of all four multiplexers.
The selection lines choose the four bits of one register and transfer them into the four-line common bus.
When S1S0 = 00, the 0 data inputs of all four multiplexers are selected and applied to the outputs that form the bus.
This causes the bus lines to receive the content of register A since the outputs of this register are connected to the 0 data inputs of the multiplexers.

## Slide 20: Common Bus System for 4 registers
Table shows the register that is selected by the bus for each of the four possible binary values of the selection lines.
S1 | S0 | Register Selected
0 | 0 | A
0 | 1 | B
1 | 0 | C
1 | 1 | D

## Slide 21: Common Bus System for 4 registers
In general, a bus system will multiplex k registers of n bits each to produce an n-line common bus.
The number of multiplexers needed to construct the bus is equal to n, the number of bits in each register.
The size of each multiplexer must be k x 1 since it multiplexes k data lines.
For example, a common bus for eight registers of 16 bits requires
Multiplexers - 16 of (8 x 1)
Select Lines - 3

## Slide 22: Tri-state Buffer (3 state Buffer)
A three-state gate is a digital circuit that exhibits three states.
Two of the states are signals equivalent to logic 1 and 0 as in a conventional gate.
The third state is high impedance state which behaves like an open circuit, which means that the output is disconnected and does not have logic significance.
Normal Input A
Control Input C
Output Y = A if C =1
High-impedance if C = 0

## Slide 23: Tri-state Buffer (3 state Buffer)
The control input determines the output state. When the control input C is equal to 1, the output is enabled and the gate behaves like any conventional buffer, with the output equal to the normal input.
When the control input C is 0, the output is disabled and the gate goes to a high-impedance state, regardless of the value in the normal input.

## Slide 24: Common Bus System using Decoder and Tri-state Buffer
2 x 4
Decoder
0
1
2
3
S1
S0
E
Select
Enable
A0
B0
C0
D0
Bus line for bit 0
1
0
1
C0

## Slide 25: Common Bus System using Decoder and Tri-state Buffer
The construction of a bus system with three-state buffers is demonstrated in previous figure.
The outputs of four buffers are connected together to form a single bus line.
The control inputs to the buffers determine which of the four normal inputs will communicate with the bus line.
The connected buffers must be controlled so that only one three-state buffer has access to the bus line while all other buffers are maintained in a high impedance state.
One way to ensure that no more than one control input is active at any given time is to use a decoder, as shown in the figure: Bus line with three state-buffers.

## Slide 26: Common Bus System using Decoder and Tri-state Buffer
When the enable input of the decoder is 0, all of its four outputs are 0, and the bus line is in a high-impedance state because all four buffers are disabled.
When the enable input is active, one of the three-state buffers will be active, depending on the binary value in the select inputs of the decoder.

## Slide 27: Arithmetic Microoperations
Arithmetic microoperations perform arithmetic operations on numeric data stored in registers.
Add Microoperation
Subtract Microoperation

## Slide 28: Arithmetic Microoperations
Symbolic Designation | Description
 | Contents of plus transferred to
 | Contents of minus transferred to
 | Complement the contents of (1’s complement)
 | 2’s complement the contents of (negate)
 | plus the 2’s complement of (subtraction)
 | Increment the content of by one
 | Decrement the content of by one

## Slide 29: Binary Adder
The digital circuit that generates the arithmetic sum of two binary numbers of any length is called a binary adder.
Example
1
1
0
1
0
1
1
1
0
1
0
0
1
1
1
0
1
+
R1
R2
C
Sum

## Slide 30: 4 – bit Binary Adder
FA
FA
FA
FA
A0
B0
A1
B1
A2
B2
A3
B3
C0
S0
S1
S2
S3
C1
C2
C3
C4
1
1
0
1
1
1
1
0
0
0
0
1
0
1
1
1
1
1
1
0
1
0
1
1
1
0
1
0
0
1
1
1
0
1
+
R1
R2
C
Sum

## Slide 31: 4 – bit Binary Adder
The binary adder is constructed with full-adder circuits connected in cascade, with the output carry from one full-adder connected to the input carry of the next full-adder.
The figure shows the interconnections of four full-adders (FA) to provide a 4-bit binary adder.
The augends bits of A and the addend bits of B are designated by subscript numbers from right to left, with subscript 0 denoting the low-order bit.
The carries are connected in a chain through the full-adders.
The input carry to the binary adder is C0 and the output carry is C4.
The S outputs of the full-adders generate the required sum bits.

## Slide 32: 4 – bit Binary Adder
An n-bit binary adder requires n full-adders.
The output carry from each full-adder is connected to the input carry of the next-high-order full-adder.
The n data bits for the A inputs come from one register (such as R1), and the n data bits for the B inputs come from another register (such as R2). The sum can be transferred to a third register or to one of the source registers (R1 or R2), replacing its previous content.

## Slide 33: Binary Adder-Subtractor
The addition and subtraction operations can be combined into one com­mon circuit by including an exclusive-OR gate with each full-adder.
Add Microoperation
Subtract Microoperation

## Slide 34: 4 – bit Binary Adder-Subtractor
FA
FA
FA
FA
A0
B0
A1
B1
A2
B2
A3
B3
C0
S0
S1
S2
S3
C1
C2
C3
C4
M
0
0
0
0
0
B0
B1
B2
B3
1
1
1
1
1
B0’
B1’
B2’
B3’

## Slide 35: 4 – bit Binary Adder-Subtractor
The mode input M controls the operation.
  when M = 0 the circuit is an Adder
  when M = 1 the circuit becomes a Subtractor
Each exclusive-OR gate receives one input M and other input from B.
  When M = 0, we have
  C0 = 0 & B ⊕ 0 = B
  The full-adders receive the value of B, the input carry is 0, and the circuit performs A plus B.
  When M = 1, we have
  C0 = 1 & B ⊕ 1 = B’
  The B inputs are all complemented and 1 is added through the input carry. The circuit performs the operation A plus the 2's complement of B.

## Slide 36: Binary Incrementer
The increment microoperation adds one to a number in a register.
1
1
0
1
1
1
1
1
0
0
0
1
+
R1
C
Sum

## Slide 37: 4 – bit Binary Incrementer
x
y
C
S
HA
x
y
C
S
HA
x
y
C
S
HA
x
y
C
S
HA
A0
1
A1
A2
A3
S0
S1
S2
S3
C4
1
0
1
1
0
1
1
1
1
0
0
0

## Slide 38: 4 – bit Binary Incrementer
As shown in figure, one of the inputs to the least significant half-adder (HA) is connected to logic-1 and the other input is connected to the least significant bit of the number to be incremented.
The output carry from one half-adder is connected to one of the inputs of the next-higher-order half-adder.
The circuit receives the four bits from A0 through A3, adds one to it, and generates the incremented output in S0 through S3.
The output carry C4 will be 1 only after incrementing binary 1111. This also causes outputs S0 through S3 to go to 0.

## Slide 39: Arithmetic Circuit
The arithmetic micro operations can be implemented in one composite arithmetic circuit.
The basic component of an arithmetic circuit is the parallel adder.
By controlling the data inputs to the adder, it is possible to obtain different types of arithmetic operations.
The output of binary adder is calculated from arithmetic sum.

## Slide 40: 4 – bit Arithmetic Circuit
Incremented content of A
S1 S0 0 1 2 3
4 x 1
MUX 3
S1 S0 0 1 2 3
4 x 1
MUX 3
S1 S0 0 1 2 3
4 x 1
MUX 3
S1 S0 0 1 2 3
4 x 1
MUX 3
C0
C1
X0
Y0
FA
C1
C2
X1
Y1
FA
C2
C3
X2
Y2
FA
C3
C4
X3
Y3
FA
D0
D1
D2
D3
Cout
Cin
S1
S0
A0
A1
A2
A3
B1
B2
B3
B0
0
1
0
1
1
0
0
0
0
1

## Slide 41: 4 – bit Arithmetic Circuit
1
1
0
1
1
1
1
0
0
1
1
1
-
1
1
0
1
1
1
1
1
+
2’s complement
Decrement using 2’s complement
1
Discard carry
1
1
0
0

## Slide 42: 4 – bit Arithmetic Circuit
Decremented content of A
S1 S0 0 1 2 3
4 x 1
MUX 3
S1 S0 0 1 2 3
4 x 1
MUX 3
S1 S0 0 1 2 3
4 x 1
MUX 3
S1 S0 0 1 2 3
4 x 1
MUX 3
C0
C1
X0
Y0
FA
C1
C2
X1
Y1
FA
C2
C3
X2
Y2
FA
C3
C4
X3
Y3
FA
D0
D1
D2
D3
Cout
Cin
S1
S0
A0
A1
A2
A3
B1
B2
B3
B0
0
1
1
1
0
1
1
1
1
0

## Slide 43: 4 – bit Arithmetic Circuit
Hardware implementation consists of:
4 full-adder circuits that constitute the 4-bit adder and four multiplexers for choosing different operations.
There are two 4-bit inputs A and B.
The four inputs from A go directly to the X inputs of the binary adder. Each of the four inputs from B is connected to the data inputs of the multiplexers. The multiplexer’s data inputs also receive the complement of B.

## Slide 44: 4 – bit Arithmetic Circuit
The other two data inputs are connected to logic-0 and logic-1.
  Logic-0 is a fixed voltage value (0 volts for TTL integrated circuits)
  Logic-1 signal can be generated through an inverter whose input is 0.
The four multiplexers are controlled by two selection inputs, S1 and S0.
The input carry Cin goes to the carry input of the FA in the least significant position. The other carries are connected from one stage to the next.
4-bit output D0…D3

## Slide 45: 4 – bit Arithmetic Circuit
When S1S0 = 00
  If Cin = 0 then D = A + B; Add
  If Cin = 1 then D = A + B + 1; Add with carry
When S1S0 = 01
  If Cin = 0 then D = A + ; Subtract with borrow
  If Cin = 1 then D = A + + 1; A + 2’s complement of B i.e. A - B

## Slide 46: 4 – bit Arithmetic Circuit
When S1S0 = 10
  Input B is neglected and all 0’s are inserted to Y inputs
  D = A + 0 + Cin
    If Cin = 0 then D = A; Transfer A
    If Cin = 1 then D = A + 1; Increment A
When S1S0 = 11
  Input B is neglected and all 1’s are inserted to Y inputs
  D = A - 1 + Cin
    If Cin = 0 then D = A - 1; 2’s compliment
    If Cin = 1 then D = A; Transfer A

## Slide 47: 4 – bit Arithmetic Circuit
Arithmetic Circuit Function
S1 | S0 | Cin | Y | D = A + Y + Cin | Microoperation
0 | 0 | 0 | B | D = A + B | Add
0 | 0 | 1 | B | D = A + B + 1 | Add with carry
0 | 1 | 0 | B’ | D = A + B’ | Subtract with borrow
0 | 1 | 1 | B’ | D = A + B’ + 1 | Subtract
1 | 0 | 0 | 0 | D = A | Transfer
1 | 0 | 1 | 0 | D = A + 1 | Increment A
1 | 1 | 0 | 1 | D = A – 1 | Decrement A
1 | 1 | 1 | 1 | D = A | Transfer A

## Slide 48: Logic Microoperations
Logic micro operations specify binary operations for strings of bits stored in registers.
These operations consider each bit of the register separately and treat them as binary variables.
Example
1
0
1
0
1
1
0
0
0
1
1
0
R1
R2
R1 after P = 1

## Slide 49: 16 Logic Microoperations
Boolean Function | Microoperation | Name
 |  | Clear
 |  | Clear
 |  | AND
 |  | AND
 |  | Transfer A
 |  | Transfer A
 |  | Transfer B
 |  | Transfer B
 |  | Exclusive-OR
 |  | Exclusive-OR
 |  | OR
 |  | OR

## Slide 50: 16 Logic Microoperations
Boolean Function | Microoperation | Name
 |  | NOR
 |  | NOR
 |  | Exclusive-NOR
 |  | Exclusive-NOR
 |  | Complement B
 |  | Complement B
 |  | Complement A
 |  | Complement A
 |  | NAND
 |  | NAND
 |  | Set to all 1’s
 |  | Set to all 1’s

## Slide 51: Hardware Implementation of Logic Circuit
4 x 1
MUX
0
1
2
3
Ai
Bi
S1
S0
Ei
S1 | S0 | Output | Operation
0 | 0 |  | AND
0 | 1 |  | OR
1 | 0 |  | XOR
1 | 1 |  | Complement
S1 | S0 | Output | Operation
0 | 0 |  | AND
0 | 1 |  | OR
1 | 0 |  | XOR
1 | 1 |  | Complement

## Slide 52: Hardware Implementation of Logic Circuit
Hardware implementation consists of four gates and a multiplexer.
Each of the four logic operations is generated through a gate that performs the required logic.
The outputs of the gates are applied to the data inputs of the multiplexer.
The two selection inputs S1 and S0 choose one of the data inputs of the multiplexer and direct its value to the output.

## Slide 53: Applications of Logic Microoperations
Selective Set Operation
The selective-set operation sets to 1 the bits in register A where there are corresponding 1's in register B.
It does not affect bit positions that have 0's in B.
The OR microoperation can be used to selectively set bits of a register.
1
0
1
0
1
1
0
0
1
1
1
0
A before
B (logic operand)
A after

## Slide 54: Applications of Logic Microoperations
Selective Complement Operation
The selective-complement operation complements bits in A where there are corresponding 1's in B.
It does not affect bit positions that have 0's in B.
The exclusive - OR microoperation can be used to selectively set bits of a register.
1
0
1
0
1
1
0
0
0
1
1
0
A before
B (logic operand)
A after

## Slide 55: Applications of Logic Microoperations
Selective Clear Operation
The selective-clear operation clears to 0 the bits in A only where there are corresponding 1's in B.
It does not affect bit positions that have 0's in B.
The corresponding logic microoperation is A ← A ∧ B’.
1
0
1
0
1
1
0
0
0
0
1
0
A before
B (logic operand)
A after

## Slide 56: Applications of Logic Microoperations
Mask Operation
The mask operation is similar to the selective-clear operation except that the bits of A are cleared only where there are corresponding 0’s in B.
The mask operation is an AND microoperation.
1
0
1
0
1
1
0
0
1
0
0
0
A before
B (logic operand)
A after

## Slide 57: Applications of Logic Microoperations
Insert Operation
The insert operation inserts a new value into a group of bits.
This is done by first masking and then ORing them with required value.
The mask operation is an AND microoperation and the insert operation is an OR microoperation.
0
1
1
0
0
0
0
0
A
B
1
0
1
0
1
1
1
1
0
0
0
0
1
0
1
0
0
0
0
0
1
0
0
1
A
B
1
0
1
0
0
0
0
0
1
0
0
1
1
0
1
0
Mask
Insert
A
A

## Slide 58: Applications of Logic Microoperations
Clear Operation
The clear operation compares the words in A and B and produces an all 0’s result if the two numbers are equal.
This operation is achieved by an exclusive-OR microoperation.
1
0
1
0
1
0
1
0
0
0
0
0
A
B
A ← A ⊕ B

## Slide 59: Shift Microoperations
Shift microoperations are used for serial transfer of data.
Used in conjunction with arithmetic, logic and other data processing operations.
The content of the register can be shifted to the left or the right.
The first flip-flop receives its binary information from the serial input.
The information transferred through the serial input determines the type of shift.

## Slide 60: Types of Shift
Logical Shift
A logical shift is one that transfers 0 through the serial input.
1 | 1 | 0 | 1
1 | 0 | 1 | 0
R1
R1
shl - logical shift left
1 | 1 | 0 | 1
0 | 1 | 1 | 0
R1
R1
shr - logical shift right

## Slide 61: Types of Shift
Circular Shift
A circular shift (also known as a rotate operation) circulates the bits of the register around the two ends without loss of information.
This is accomplished by connecting the serial output of the shift register to its serial input.
1 | 1 | 0 | 1
1 | 0 | 1 | 1
R1
R1
cil - circular shift left
1 | 1 | 0 | 1
1 | 1 | 1 | 0
R1
R1
cir - circular shift right

## Slide 62: Types of Shift
Arithmetic Shift
An arithmetic shift is a micro-operation that shifts a signed binary number to the left or right.
An arithmetic shift-left multiplies a signed binary number by 2.
An arithmetic shift-right divides the number by 2.
1 | 1 | 0 | 1
1 | 0 | 1 | 0
R1
R1
ashl - arithmetic shift left
1 | 1 | 0 | 1
1 | 1 | 1 | 0
R1
R1
ashr - arithmetic shift right

## Slide 63: 4 - bit Combinational Circuit Shifter
S
0
1
MUX
S
0
1
MUX
S
0
1
MUX
S
0
1
MUX
A0
A1
A2
A3
H0
H1
H2
H3
Select
0 – Shift right
1 – Shift left
IR
IL
S | H0 | H1 | H2 | H3
0 | IR | A0 | A1 | A2
1 | A1 | A2 | A3 | IL
0
1
0
1
1
0
1
0
1

## Slide 64: 4 - bit Combinational Circuit Shifter
The 4-bit shifter has four data inputs, A0 through A3 and four data outputs, H0 through H3.
There are two serial inputs, one for shift left (IL) and the other for shift right (IL).
When the selection input S = 0, the input data are shifted right (down in the diagram).
When S = 1, the input data are shifted left (up in the diagram).
The two serial inputs can be controlled by another multiplexer to provide the three possible types of shifts.

## Slide 65: 4 – bit Arithmetic Logic Shift Unit
Instead of having individual registers performing the micro operations directly, computer systems employ a number of storage registers connected to a common operational unit called an arithmetic logic unit, abbreviated ALU.
To perform a microoperation, the contents of specified registers are placed in the inputs of the common ALU.
The ALU performs an operation and the result of the operation is then transferred to a destination register.
The arithmetic, logic, and shift circuits introduced in previous sections can be combined into one ALU with common selection variables.

## Slide 66: 4 – bit Arithmetic Logic Shift Unit
0
1
2
3
4 x 1
MUX
One stage of arithmetic circuit
One stage of logic circuit
S2
S3
S1
S0
Ai
Bi
Ai-1
Ai+1
Ci
Ci +1
Di
Ei
Fi
shr
shl
Select

## Slide 67: 4 – bit Arithmetic Logic Shift Unit
ALU Function
S3 | S2 | S1 | S0 | Cin | Operation | Function
0 | 0 | 0 | 0 | 0 | F = A | Transfer A
0 | 0 | 0 | 0 | 1 | F = A + 1 | Increment A
0 | 0 | 0 | 1 | 0 | F = A + B | Addition
0 | 0 | 0 | 1 | 1 | F = A + B + 1 | Add with carry
0 | 0 | 1 | 0 | 0 | F = A + B’ | Subtract with borrow
0 | 0 | 1 | 0 | 1 | F = A + B’ + 1 | Subtraction
0 | 0 | 1 | 1 | 0 | F = A – 1 | Decrement

## Slide 68: 4 – bit Arithmetic Logic Shift Unit
S3 | S2 | S1 | S0 | Cin | Operation | Function
0 | 0 | 1 | 1 | 1 | F = A | Transfer A
0 | 1 | 0 | 0 | x | F = | AND
0 | 1 | 0 | 0 | x |  | AND
0 | 1 | 0 | 1 | x | F = | OR
0 | 1 | 0 | 1 | x |  | OR
0 | 1 | 1 | 0 | x | F = A ⊕B | XOR
0 | 1 | 1 | 1 | X | F = A’ | Complement A
1 | 0 | x | x | x | F = shr A | Shift right A into F
1 | 1 | x | x | x | F = shl A | Shift left A into F

## Slide 69: Questions asked in GTU exam
What do you mean by register transfer? Explain in detail. Also discuss three-state bus buffer.
List and explain types of shift operations on accumulator.
Define RTL. Explain how register transfer takes place in basic computer system
What is multiplexing? Explain the multiplexing of control signals in ALU.
Explain how complement number system is useful in computer system. Discuss any one complement number system with example.
Draw the block diagram of 4-bit arithmetic circuit and explain it in detail.
Explain shift micro operations and Draw neat and clean diagram for 4-bit combinational circuit shifter.
Explain hardware implementation of common bus system using three state buffers. Mention assumptions if required.
Explain 4-bit adder-subtractor with diagram.
Explain floating point representation.
What is a Digital Computer System? Explain the role of binary number system in it.
Design a digital circuit for 4-bit binary adder.

## Slide 70: Questions asked in GTU exam
Represent (8620)10 in (1) binary (2) Excess-3 code and (3) 2421 code.
Explain selective set, selective complement and selective clear.
How negative integer number represented in memory? Explain with suitable example.
Explain Micro operation.
What does this mean: R2 ← R1?
What does this mean: T0: R4 ← R0?
What is a Bus?
What is an ALU?
"Represent the following conditional control statement(s) by two register transfer statements with control function. If (P=1) then (R1 ← R2) else if (Q=1) then (R1 ← R3)"
State true or false: In binary number system, B - A is equivalent to B + A' + 1.
Draw a diagram of 4-bit binary incrementer and explain it briefly.