## Slide 1: Unit-2 Combinational Digital Circuits
krunal.vyas@darshan.ac.in
9601901005
Computer Engineering Department
Prof. Krunal D. Vyas
Digital Fundamentals (DF)
GTU # 3130704

## Slide 2

Looping
Outline
  Standard representation for logic functions
    SOP, POS
  Simplification using K-Map
    2-variable, 3-variable, 4-variable, VEM
  Q-M Method (Tabulation Method)
  Adders, Subtractors
    Half adder, Full adder, Half Subtractor, Full Subtractor
  Combinational Circuits
    Converters, Comparators, Generators
  Multiplexer/De-multiplexer, Encoder/Decoder

## Slide 3: Standard representation for logic functions
Section - 1

## Slide 4: Boolean functions & representation
Sum-of-products (SOP) form (Disjunctive Normal Form)
Products-of-sums (POS) form (Conjunctive Normal Form)

## Slide 5: Boolean functions & representation
Standard sum-of-products form (Minterm)
Contains all the variables of the function either in complemented or uncomplemented form.
Variable appears in uncomplemented form if it has a value of 1 in the combination and appears in complemented form if it has a value of 0 in the combination
Sum of minterms whose value is equal to 1 is the standard sum of products form of the function.
Minterms are denoted as m0, m1, m2, …,
For 3 variable function, m0=, m1=, m2=, m3=, m4=, m5=, m6=, and m7=
Value of Minterm = 1

## Slide 6: Boolean functions & representation
Canonical SOP form is shown by the sum of minterms for which the function equals 1.
f(A,B,C) = m1 + m2 + m3 + m5
Or
f(A,B,C) =
Standard product-of-sum form (Maxterm)
Derived by considering the combinations of which f = 0
Each term is a sum of all the variables
Variable appears in uncomplemented form if it has a value of 0 in the combination and appears in complemented form if it has a value of 1 in the combination

## Slide 7: Boolean functions & representation
A sum term which contains each of the n variables in either complemented or uncomplemented form is called a maxterm.
Maxterms are denoted as M0, M1, M2, …,
f(A,B,C) = M0M1M6M7
Or
f(A,B,C) =
Value of Maxterm = 0

## Slide 8: Simplification using K-Map
Section - 2

## Slide 9: Introduction to K-Maps
Simplification of Boolean functions leads to simpler (and usually faster) digital circuits.
Simplifying Boolean functions using identities is time-consuming and error-prone.
This special section presents an easy, systematic method for reducing Boolean expressions.
A K-Map is a matrix consisting of rows and columns that represent the output values of a Boolean function.
The output values placed in each cell are derived from the minterms of a Boolean function.
A minterm is a product term that contains all of the function’s variables exactly once, either complemented or not complemented.

## Slide 10: 2 – Variable K-Map
The two variables A and B have four possible combinations that can be represented by the map as follows
A
B
0
1
0
1
0
1
2
3
A | B | Minterm
0 | 0 | m0 = A’B’
0 | 1 | m1 = A’B
1 | 0 | m2 = AB’
1 | 1 | m3 = AB

## Slide 11: 3 – Variable K-Map
The three variables A, B and C have eight possible combinations that can be represented by the map as follows
AB
C
00
10
0
1
0
1
2
3
A | B | C | Minterm
0 | 0 | 0 | m0 = A’B’C’
0 | 0 | 1 | m1 = A’B’C
0 | 1 | 0 | m2 = A’BC’
0 | 1 | 1 | m3 = A’BC
1 | 0 | 0 | m4 = AB’C’
1 | 0 | 1 | m5 = AB’C
1 | 1 | 0 | m6 = ABC’
1 | 1 | 1 | m7 = ABC
01
11
4
5
6
7
Minterm Number

## Slide 12: 4 – Variable K-Map
The four variables A, B, C and D have sixteen possible combinations that can be represented by the map as follows
A | B | C | D | Minterm
0 | 0 | 0 | 0 | m0 = A’B’C’D’
0 | 0 | 0 | 1 | m1 = A’B’C’D
0 | 0 | 1 | 0 | m2 = A’B’CD’
0 | 0 | 1 | 1 | m3 = A’B’CD
0 | 1 | 0 | 0 | m4 = A’BC’D’
0 | 1 | 0 | 1 | m5 = A’BC’D
0 | 1 | 1 | 0 | m6 = A’BCD’
0 | 1 | 1 | 1 | m7 = A’BCD
A | B | C | D | Minterm
1 | 0 | 0 | 0 | m8 = AB’C’D’
1 | 0 | 0 | 1 | m9 = AB’C’D
1 | 0 | 1 | 0 | m10 = AB’CD’
1 | 0 | 1 | 1 | m11 = AB’CD
1 | 1 | 0 | 0 | m12 = ABC’D’
1 | 1 | 0 | 1 | m13 = ABC’D
1 | 1 | 1 | 0 | m14 = ABCD’
1 | 1 | 1 | 1 | m15 = ABCD
AB
CD
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11

## Slide 13: Reduce Boolean Expression
Consider the function:
Its K-Map is given below.
What is the largest group of 1’s that is a power of 2?
This grouping tells us that changes in the variables A and B have no influence upon the value of the function: They are irrelevant.
AB
C
00
10
0
1
0
1
2
3
01
11
4
5
6
7
1
1
1
1

## Slide 14: Examples (SOP)
1
1
AB
CD
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
1
1
1
1
AB
C
00
10
0
1
01
11
0
1
2
3
4
5
6
7

## Slide 15: Examples (SOP)
AB
CD
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
1
1
1
1
1
AB
CD
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
1
1
1

## Slide 16: Example (POS)
f(A,B,C,D) =
AB
CD
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
0
0
0
0
0
0
0
0

## Slide 17: Don’t care conditions
Suppose we are given a problem of implementing a circuit to generate a logical 1 when a 2, 7, or 15 appears on a four-variable input.
A logical 0 should be generated when 0, 1, 4, 5, 6, 9, 10, 13 or 14 appears.
The input conditions for the numbers 3, 8, 11 and 12 never occur in the system. This means we don’t care whether inputs generate logical 1 or logical 0.
Don’t care combinations are denoted by ‘x’ in K-Map which can be used for the making groups.
The above example can be represented as
AB
CD
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
1
1
1
x
x
f(A,B,C,D) = + d(3,8,11,12)
x
x

## Slide 18: Example (Don’t care)
WX
YZ
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
1
1
1
F(W,X,Y,Z) = + d(0,2,5)
x
x
1
1
x

## Slide 19: Variable-Entered Map (VEM)
Variable-entered map can be used to plot an n-variable problem on n – 1 variable map
Possible to reduce the map dimension by two or three in some cases
Advantage of using VEM occurs in design problems involving multiplexers
Map-entered variable for 3 variable function
Consider the function
Considering value of to be function of map location with the variable and plotting 2 variable map.
A
B
0
1
0
1
X=1 if C’=1
X=1 if C’=1
X=1 if C’=1 or if C = 1
X=0
A
B
0
1
0
1
C’
C’
0
C + C’

## Slide 20: Reducing Expressions with VEM (Example)
Choose groups of similar terms to cover all nonzero terms appearing in the map except “don’t care” terms.
Rest complete process is similar to K-Map
AB
C
00
10
0
1
01
11
D+D’
D
D
D
D

## Slide 21: Reducing Expressions with VEM (Example)
AB
C
00
10
0
1
01
11
D+D’
D
D’
D’
D+D’
D’
D’

## Slide 22: Reducing Expressions with VEM (Example)
f
AB
CD
00
10
00
01
01
11
11
10
E
E
E’
E’
E+E’
E+E’
E+E’
E’

## Slide 23: Q-M Method (Tabulation Method)
Section - 3

## Slide 24: Tabulation Method (Quine-McCluskey Method)
Fundamental idea for tabulation method is combining theorem.
The above theorem is applied repeatedly to all adjacent pairs of terms which results in prime implicants.
Consider the minimization of the expression
= A’B’C’ + A’B’C + AB’C’ + AB’C
= A’B’(C + C’) + AB’(C + C’)
= A’B’ + AB’
= B’(A + A’)
= B’

## Slide 25: Procedure for minimization using Tabulation Method
List all the minterms.
Arrange all minterms in groups of the same number of 1s in their binary representation in column 1. Start with the least number of 1s group and continue with groups of increasing number of 1s.
Compare each term of the lowest index group with every term in the succeeding group. Whenever possible, combine the two terms being compared by means of the combining theorem. Two terms from adjacent groups are combinable, if their binary representations differ by just a single digit in the same position; the combined terms consist of the original fixed representation with the differing one replaced by a dash (-). Place a check mark (√) next to every term, which has been combined with at least one term and write the combined terms in column 2. Repeat this by comparing each term in a group of index i with every term in the group of index i + 1, until all possible applications of the combining theorem have been exhausted.

## Slide 26: Procedure for minimization using Tabulation Method
Compare the terms generated in step 3 in the same fashion; combine two terms which differ by only a single 1 and whose dashes are in the same position to generate a new term. Two terms with dashes in different positions cannot be combined. Write the new terms in column 3 and put a check mark next to each term which has been combined in column 2. Continue the process with terms in columns 3, 4 etc. until no further combinations are possible. The remaining unchecked terms constitute the set of prime implicants of the expression.
List all the prime implicants and draw the prime implicant chart. (The don’t cares if any should not appear in the prime implicant chart).
Obtain the essential prime implicants and write the minimal expression.

## Slide 27: Tabulation Method (Example)
Step – 1: List all minterms
Minterms | Binary Designation
0 | 0 0 0 0
1 | 0 0 0 1
6 | 0 1 1 0
7 | 0 1 1 1
8 | 1 0 0 0
9 | 1 0 0 1
13 | 1 1 0 1
14 | 1 1 1 0
15 | 1 1 1 1
Step – 2: Arrange all minterms in groups of same number of 1s
Column 1 |  | 
Index | Minterms | Binary Designation
Index 0 | 0 | 0 0 0 0
Index 1 | 1 8 | 0 0 0 1 1 0 0 0
Index 2 | 6 9 | 0 1 1 0 1 0 0 1
Index 3 | 7 13 14 | 0 1 1 1 1 1 0 1 1 1 1 0
Index 4 | 15 | 1 1 1 1

## Slide 28: Tabulation Method (Example) Cont..
Step – 3: Compare each term of the lowest index group with every term in the succeeding group till no change
Column 2 | 
Pairs | A B C D
0, 1 0, 8 | 0 0 0 _ _ 0 0 0
1, 9 8, 9 | _ 0 0 1 1 0 0 _
6, 7 6, 14 9, 13 | 0 1 1 _ _ 1 1 0 1 _ 0 1
7, 15 13, 15 14, 15 | _ 1 1 1 1 1 _ 1 1 1 1 _
Column 1 |  | 
Index | Minterms | Binary Designation
Index 0 | 0 | 0 0 0 0
Index 1 | 1 8 | 0 0 0 1 1 0 0 0
Index 2 | 6 9 | 0 1 1 0 1 0 0 1
Index 3 | 7 13 14 | 0 1 1 1 1 1 0 1 1 1 1 0
Index 4 | 15 | 1 1 1 1
√
√
√
√
√
√
√
√
√

## Slide 29: Tabulation Method (Example) Cont..
Pairs | A B C D
0, 1 0, 8 | 0 0 0 _ _ 0 0 0
1, 9 8, 9 | _ 0 0 1 1 0 0 _
6, 7 6, 14 9,13 | 0 1 1 _ _ 1 1 0 1 _ 0 1
7, 15 13, 15 14, 15 | _ 1 1 1 1 1 _ 1 1 1 1 _
Step – 4: Compare the terms generated in step 3 in the same fashion until no further combinations are possible
Quads | A B C D
0, 1, 8, 9 | _ 0 0 _
6, 7, 14, 15 | _ 1 1 _
√
√
√
√
√
√
√
√
P
Q
R
S

## Slide 30: Tabulation Method (Example) Cont..
Step – 5: List all prime implicants and draw prime implicants chart
Prime Implicants : P(BC), Q(B’C’), R(ABD), S(AC’D)
 | √ | √ | √ | √ | √ | √ |  | √ | √
PIs | 0 | 1 | 6 | 7 | 8 | 9 | 13 | 14 | 15
P (6,7,14,15) |  |  | x | x |  |  |  | x | x
Q (0,1,8,9) | x | x |  |  | x | x |  |  | 
R (13,15) |  |  |  |  |  |  | x |  | x
S (9,13) |  |  |  |  |  | x | x |  | 
Step – 6: Obtain essential prime implicants and minimal expression
Essential Prime Implicants : P(BC)
, Q(B’C’)
Minimal expression : P + Q + R = BC + B’C’ + ABD
OR P + Q + S = BC + B’C’ + AC’D
As minterm 13 is covered by R and S

## Slide 31: Realizing Logic Function with Gates
Implement AB’ + C’D using AND, OR & Invert Gates
A
B
C
D

## Slide 32: Converting AND/OR/Invert Logic to NAND/NOR Logic
Draw the circuit in AOI logic.
If NAND hardware is chosen, add a circle at the output of each AND gate and at the inputs to all the OR gates.
If NOR hardware is chosen, add a circle at the output of each OR gate and at the inputs to all the AND gates.
Add or subtract an inverter on each line that received a circle in steps 2 or 3 so that the polarity of signals on those lines remains unchanged from that of the original diagram.
Replace bubbled OR by NAND and bubbled AND by NOR.
Eliminate double inversions.

## Slide 33: Converting AND/OR/Invert Logic to NAND/NOR Logic (Example)
Implement the following AOI logic using NAND logic
Put a circle at the output of each AND gate and at the inputs to all OR gates

## Slide 34: Converting AND/OR/Invert Logic to NAND/NOR Logic (Example)
Add an inverter to each of the lines that received only one circle at input so that polarity remains unchanged.

## Slide 35: Converting AND/OR/Invert Logic to NAND/NOR Logic (Example)
Replace bubbled OR gates and NOT gates by NAND gates.

## Slide 36: Adders, Subtractors
Section - 4

## Slide 37: Half Adder
A combinational circuit which adds two one-bit binary numbers is called a half-adder.
The sum column resembles like an output of the XOR gate.
The carry column resembles like an output of the AND gate.
Limitations:
  In multi-digit addition we have to add two bits along with the carry of previous digit addition. Such addition requires addition of 3 bits. This is not possible in half-adders.
Inputs |  | Outputs | 
A | B | Sum | Carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
S = A ⊕ B
C = AB
A
B

## Slide 38: Full Adder
The full-adder adds the bits A and B and the carry from the previous column called carry-in Cin and outputs the sum bit S and the carry bit called carry-out Cout.
Inputs |  |  | Outputs | 
A | B | Cin | S | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
S = A’B’Cin + A’BCin’ + AB’Cin’ + ABCin
= (AB’ + A’B)Cin’ + (AB + A’B’)Cin
= (A ⊕ B)Cin’ + (A ⊕ B)’Cin
= A ⊕ B ⊕ Cin
Cout = A’BCin + AB’Cin + ABCin’ + ABCin
= AB + (A ⊕ B)Cin

## Slide 39: Full Adder – Logical Diagram
A
B
Cin
S = A ⊕ B ⊕ Cin
Cout = AB + (A ⊕ B)Cin
Half Adder
Half Adder
S = A ⊕ B ⊕ Cin
Cout = AB + (A ⊕ B)Cin

## Slide 40: Half Subtractor
Subtracts one bit from the other and produces the difference.
Other output is to specify if 1 is borrowed.
Limitation:
  Half subtractor can be used only for LSB subtraction.
Inputs |  | Outputs | 
A | B | d | b
0 | 0 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
d = A ⊕ B
b = A’B
A
B

## Slide 41: Full Subtractor
Full subtractor is a combinational circuit with 3 inputs (A, B, bi)
Subtraction = A – B – bi
Inputs |  |  | Outputs | 
A | B | bi | d | b
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1
d = A’B’bi + A’Bbi’ + AB’bi’ + ABbi
= (AB’ + A’B)bi’ + (AB + A’B’)bi
= (A ⊕ B)bi’ + (A ⊕ B)’bi
= A ⊕ B ⊕ bi
b = A’B’bi + A’Bbi’ + A’Bbi + ABbi
= A’B(bi + bi’) + (AB + A’B’)bi
= A’B + (A ⊕ B)’bi

## Slide 42: Full Subtractor – Logical Diagram
A
B
bi
d = A ⊕ B ⊕ bi
b = A’B + (A ⊕ B)’bi
d = A ⊕ B ⊕ bi
b = A’B + (A ⊕ B)’bi

## Slide 43: Binary Parallel Adder
FA3
B3
A3
S3
C3
FA2
B2
A2
S2
C2
C1
FA1
B1
A1
S1
Cin
FA4
B4
A4
S4
C4
Example: A = 1010, B = 1101
A4 A3 A2 A1 = 1010
B4 B3 B2 B1 = 1101
0
0
0
1
1
1
1
1
0
1
0
1
0
1
0
1
0

## Slide 44: Binary Parallel Subtractor
FA4
S4
Cout
B4
A4
FA3
S3
C3
B3
A3
Cin= 1
FA1
S1
C1
B1
A1
FA2
S2
C2
B2
A2
Example: A = 1101, B = 1011
A4 A3 A2 A1 = 1101
B4 B3 B2 B1 = 1011
1
1
0
1
1
0
1
1
0
0
1
0
0
1
1
0
0
1
0
1

## Slide 45: Binary Adder-Subtractor
FA4
S4
C4
B4
A4
FA3
S3
C3
B3
A3
FA2
S2
C2
B2
A2
FA1
S1
C1
Cin
B1
A1
When M = 0, Circuit is an adder.
When M = 1, Circuit becomes a subtractor.
M
M | Bi | O/P
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 46: Look Ahead Carry Adder
Speeds up the process by eliminating the ripple carry delay.
The method of speeding up the addition process is based on: carry generate and carry propagate functions.
Consider one full adder stage; say the nth stage of a parallel adder shown in below Figure.
HA
HA
An
Bn
Cn
An Bn = Gn
An ⊕ Bn = Pn
Pn Cn = Co
Cn+1 = (An ⊕ Bn) Cn + An Bn
Sn = An ⊕ Bn ⊕ Cn

## Slide 47: Look Ahead Carry Adder
Sn = Pn ⊕ Cn where Pn = An ⊕ Bn
Cn+1 = Gn + Pn Cn where Gn = An Bn
Possible to express the output carry of a higher significant stage in terms of applied input variables A, B and carry-in to the LSB adder.
Based on these, the expressions for the carry-outs of various full adders are as follows:
C2 = G1 + P1 C1
C3 = G2 + P2 C2
= G2 + P2 (G1 + P1 C1)
= G2 + P2 G1 + P2 P1 C1
C4 = G3 + P3 C3 = G3 + P3 G2 + P3 P2 G1 + P3 P2 P1 C1
C5 = G4 + P4 C4 = G4 + P4 G3 + P4 P3 G2 + P4 P3 P2 G1 + P4 P3 P2 P1 C1

## Slide 48
B4
A4
P4
G4
B3
A3
P3
G3
B2
A2
P2
G2
B1
A1
P1
G1
P4
C4
S4
C5
C5
P3
C3
S3
P2
C2
S2
P1
S1
C1
C1
Look ahead carry adder

## Slide 49: Combinational Circuits
Section - 5

## Slide 50
4-bit Binary |  |  |  | 4-bit Gray |  |  | 
B4 | B3 | B2 | B1 | G4 | G3 | G2 | G1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 1 | 1 | 0 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1 | 0 | 0 | 0
Binary to Gray Code Converter

## Slide 51: Binary to Gray Code Converter
K-Map for G4, G3, G2, G1 function and their minimization are as follows:
B4B3
B2B1
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
B4B3
B2B1
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
G3 = B4’B3 + B4B3’ = B4 B3
G4 = B4

## Slide 52: Binary to Gray Code Converter
B4B3
B2B1
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
B4B3
B2B1
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
G1 = B2’B1 + B2B1’ = B2 B1
G2 = B3’B2 + B3B2’ = B3 B2

## Slide 53: Binary to Gray Code Converter
Logic diagram for binary to Gray code converter is as follows:
B4
B3
B2
B1
G4
G3
G2
G1
G3 = B4’B3 + B4B3’ = B4 B3
G4 = B4
G1 = B2’B1 + B2B1’ = B2 B1
G2 = B3’B2 + B3B2’ = B3 B2

## Slide 54: BCD to Excess-3 Code Converter
8421 BCD |  |  |  | XS - 3 |  |  | 
B4 | B3 | B2 | B1 | X4 | X3 | X2 | X1
0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 0 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 0 | 0

## Slide 55: BCD to Excess-3 Code Converter
K-Map for X4, X3, X2, X1 function and their minimization are as follows:
B4B3
B2B1
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
B4B3
B2B1
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
1
1
x
x
x
1
1
1
1
1
1
1
1
X3 = B3B2’B1’ + B3’ B1 + B3’ B2
X4 = B4 + B3B2 + B3B1
x
x
x
x
x
x
x
x
x

## Slide 56: BCD to Excess-3 Code Converter
B4B3
B2B1
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
B4B3
B2B1
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
1
1
x
x
x
1
1
1
1
1
1
1
1
X1 = B1’
X2 = B2’B1’ + B2B1
x
x
x
x
x
x
x
x
x

## Slide 57: BCD to Excess-3 Code Converter
Logic diagram for a BCD to Excess-3 is as follows
B3
B2
B1
B2’
B1’
B1
B2
X2
X4
B4
B3
B3’
B2
X3
B3
B3’
B2’
B1’
B1
X1
B1’

## Slide 58: Comparators
A comparator is a logic circuit used to compare the magnitudes of two binary numbers.
Comparator circuit provides 3 outputs
  A = B
  A > B
  A < B
X-NOR gate is a basic comparator (the output is 1 if and only if the input bits coincide).
2 binary numbers are equal if and only if all their corresponding bits coincide.
E.g. A3A2A1A0 and B3B2B1B0 are equal if and only if A3=B3, A2=B2, A1=B1 and A0=B0
Equality = (A3B3) (A2B2) (A1B1) (A0B0)

## Slide 59: 1-bit Magnitude Comparator
Let the 1-bit numbers be A = A0 and B = B0
If A0 = 1 and B0 = 0 then A > B
A > B : G = A0B0’
If A0 = 0 and B0 = 1 then A < B
A < B : L = A0’B0
If A0 = 1 and B0 = 1 (coincides) then A = B
A = B : E = A0 B0
A0 | B0 | L | E | G
0 | 0 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0
A0
B0
A < B(L)
A = B(E)
A > B(G)

## Slide 60: 2-bit Magnitude Comparator
Let the two 2-bit numbers be A = A1A0 and B = B1B0
If A1 = 1 and B1 = 0, then A > B or
If A1 and B1 coincide and A0 = 1 and B0 = 0, then A > B.
A > B : G = A1B1’ + (A1 ⊙ B1) A0B0’
If A1 = 0 and B1 = 1, then A < B or
If A1 and B1 coincide and A0 = 0 and B0 = 1, then A < B.
A < B : L = A1’B1 + (A1 ⊙ B1) A0’B0
If A1 and B1 coincide and if A0 and B0 coincide then A = B.
A = B : E = (A1 ⊙ B1)(A0 ⊙ B0)

## Slide 61: 2-bit Magnitude Comparator
A0
B0
A1
B1
A1
B1’
A0
B0’
A0’
B0
B1
A1’
A < B(L)
A = B(E)
A > B(G)

## Slide 62: Parity Generator
Binary data, when transmitted and processed is susceptible to noise that can alter its 1s to 0s and 0s to 1s.
To detect such errors, an additional bit called parity bit is added to the data bits and the word containing the data bits and the parity bit is transmitted.
At the receiving end the number of 1s in the word received are counted and the error, if any, is detected.
0 | 0 | 1 | 1
0 | 0 | 1 | 0
Even Parity
Odd Parity
Data
Data
Parity bit
Parity bit

## Slide 63: 3-bit parity generator using even parity bit
Inputs |  |  | Outputs parity bit (f)
A | B | C | 
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1
AB
C
00
10
0
1
01
11
1
1
1
1
A
B
C
f

## Slide 64: Multiplexer/De-multiplexer, Encoder/Decoder
Section - 6

## Slide 65: Multiplexer
A multiplexer(MUX) is a device that allows digital information from several sources to be routed onto a single line for transmission over that line to a common destination.
Consider an integer ‘m’, which is constrained by the following relation:
m = 2n, where m and n are both integers.
A m-to-1 Multiplexer has
  m Inputs: I0, I1, I2, ................ I(m-1)
  One Output: Y
  n Control inputs: S0, S1, S2, ...... S(n-1)
  One (or more) Enable input(s)
Such that Y may be equal to one of the inputs, depending upon the control inputs.

## Slide 66: 4-to-1 Multiplexer
I0
I1
I2
I3
S0
S1
Y
1 output
n control inputs
2n inputs
Enable (G)
4 x 1 MUX
Select Inputs |  | Output
S1 | S0 | Y
0 | 0 | I0
0 | 1 | I1
1 | 0 | I2
1 | 1 | I3
Y = S1’S0’I0 + S1’S0I1 + S1S0’I2 + S1S0I3
0
0
I0

## Slide 67: 4 x 1 MUX Actual Circuit
I3
I2
I1
I0
S0
S1
Enable (G)
Y

## Slide 68: Logic function generator using Multiplexer
Implement the following function using 8 to 1 MUX
F(x,y,z) =
S2 | S1 | S0 | F
x | y | z | 
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
8 x 1 MUX
D0
D1
D2
D3
D4
D5
D6
D7
S0
S1
S2
z
y
x
1
1
1
1
0
0
0
0
Output = F

## Slide 69: Logic function generator using Multiplexer (Method)
Multiplexer with n-data select inputs can implement any function of n + 1 variables.
The first n variables of the function as the select inputs and to use the least significant input variable and its complement to drive some of the data inputs.
If the single variable is denoted by D, each data output of the multiplexer will be D, D’, 1, or 0.
Suppose, we wish to implement a 4-variable logic function using a multiplexer with three data select inputs.
Let the input variables be A, B, C, and D; D is the LSB.
A truth table for the function F(A, B, C, D) is constructed with ABC has the same value twice once with D = 0 and again with D = 1.

## Slide 70: Logic function generator using Multiplexer (Method)
The following rules are used to determine the connections that should be made to the data inputs of the multiplexer.
  If F = 0 both times when the same combination of ABC occurs, connect logic 0 to the data input selected by that combination.
  If F = 1 both times when the same combination of ABC occurs, connect logic 1 to the data input selected by that combination.
  If F is different for the two occurrences of a combination of ABC, and if F = D in each case, connect D to the data input selected by that combination.
  If F is different for the two occurrences of a combination of ABC, and if F = D’ in each case, connect D’ to the data input selected by that combination.

## Slide 71
Implement the following function using 8 to 1 MUX
F =
S2 | S1 | S0 | D | F | 
A | B | C |  |  | 
0 0 | 0 0 | 0 0 | 0 1 | 1 1 | F = 1
0 0 | 0 0 | 1 1 | 0 1 | 1 1 | F = 1
0 0 | 1 1 | 0 0 | 0 1 | 1 0 | F = D’
0 0 | 1 1 | 1 1 | 0 1 | 0 0 | F = 0
1 1 | 0 0 | 0 0 | 0 1 | 0 0 | F = 0
1 1 | 0 0 | 1 1 | 0 1 | 1 1 | F = 1
1 1 | 1 1 | 0 0 | 0 1 | 0 0 | F = 0
1 1 | 1 1 | 1 1 | 0 1 | 1 1 | F = 1
8 x 1 MUX
D0
D1
D2
D3
D4
D5
D6
D7
S0
S1
S2
C
B
A
1
D’
0
1
1
0
0
1
Output = F

## Slide 72: Demultiplexer
A demultiplexer(DEMUX) is a device that allows digital information from one source to be routed onto a multiple lines for transmission over different destinations.
Consider an integer ‘m’, which is constrained by the following relation:
m = 2n, where m and n are both integers.
A 1-to-m Demultiplexer has
  One Input: D
  m Outputs: O0, O1, O2, ................ O(m-1)
  n Control inputs: S0, S1, S2, ...... S(n-1)
  One (or more) Enable input(s)
Such that D may be transfer to one of the outputs, depending upon the control inputs.

## Slide 73: 1-to-4 Demultiplexer
D
O0
O1
O2
O3
1x4 DEMUX
S1
S0
Select code |  | Outputs |  |  | 
S1 | S0 | O3 | O2 | O1 | O0
0 | 0 | 0 | 0 | 0 | D
0 | 1 | 0 | 0 | D | 0
1 | 0 | 0 | D | 0 | 0
1 | 1 | D | 0 | 0 | 0
D
S1
S1’
S0
S0’
O0 = D S 1’ S0’
O1 = D S 1’ S0
O2 = D S 1 S0’
O3 = D S 1 S0

## Slide 74: Decoder
A decoder is a logic circuit that accepts a set of inputs which represents a binary number and activates the only output that corresponds to the input number.
In other words, a decoder circuit looks at its inputs, determines which binary number is present there, and activates the specific output which corresponds to that number; all other outputs remain inactive.
In its general form, a decoder has N input lines to handle N bits and M output lines such that only one output line is activated for each one of the possible combinations of inputs.
I0
I1
I2
IN-2
IN-1
.
.
.
O0
O1
O2
OM-2
OM-1
.
.
.
N inputs
M outputs
Decoder
M = 2N

## Slide 75: 3-Line to 8-Line Decoder
Inputs |  |  | Outputs |  |  |  |  |  |  | 
A | B | C | D0 A’B’C’ | D1 A’B’C | D2 A’BC’ | D3 A’BC | D4 AB’C’ | D5 AB’C | D6 ABC’ | D7 ABC
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
3 to 8 line decoder can be implemented using AND gates to achieve active-HIGH output.
For active-LOW outputs, NAND gates are used.

## Slide 76
D7 = ABC
D6 = ABC’
D5 = AB’C
D4 = AB’C’
D3 = A’BC
D2 = A’BC’
D1 = A’B’C
D0 = A’B’C’
A
A’
B
B’
C
C’

## Slide 77: Encoder
Device to convert familiar numbers or symbols into coded format.
It has a number of input lines, only one of which is activated at a given time, and produces an N-bit output code depending on which input is activated.
Figure shows the block diagram of an encoder with M inputs and N outputs.
I0
I1
I2
IM-2
IM-1
.
.
.
O0
O1
O2
ON-2
ON-1
.
.
.
M inputs
N outputs
Encoder
M = 2N

## Slide 78: Priority Encoder
A priority encoder is a logic circuit that responds to just one input in accordance with some priority system, among all those that may be simultaneously HIGH.
The most common priority system is based on the relative magnitudes of the inputs; whichever decimal input is the largest, is the one that is encoded.
For example, if both decimal 3 and decimal 4 are activated simultaneously, then a priority encoder would encode decimal 4.
Inputs |  |  |  | Outputs |  | 
D0 | D1 | D2 | D3 | A | B | V
0 | 0 | 0 | 0 | x | x | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
x | 1 | 0 | 0 | 0 | 1 | 1
x | x | 1 | 0 | 1 | 0 | 1
x | x | x | 1 | 1 | 1 | 1

## Slide 79: Priority Encoder
D0D1
D2D3
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
1
x
1
1
1
1
1
1
1
1
1
1
1
D0D1
D2D3
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
1
x
1
1
1
1
1
1
1
1
1
A = D3 + D2
B = D3 + D2’ D1

## Slide 80: Priority Encoder
D0D1
D2D3
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
1
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
V = D3 + D2 + D1 + D0
D3
D2
D1
D0
B = D3 + D2’ D1
A = D3 + D2
V = D3 + D2 + D1 + D0

## Slide 81: Serial Adder
Shift register A
Shift register B
x
y
z
S
C
Q
D
C
SO
SO
SI
SI
CLK
Clear
Shift
control
Serial
input
FA

## Slide 82: Arithmetic Logic Unit (ALU)
A
A4
A3
A2
A1
B4
B3
B2
B1
B
S2
S1
S0
Cin
(Mode - select)
(Function - select)
(Input carry)
(Output carry)
Cout
F4
F3
F2
F1
F
Arithmetic Logic Unit (ALU)

## Slide 83: Arithmetic Logic Unit (ALU)
Selection |  |  |  | Output | Function
S2 | S1 | S0 | Cin |  | 
0 | 0 | 0 | 0 | F = A | Transfer A
0 | 0 | 0 | 1 | F = A + 1 | Increment A
0 | 0 | 1 | 0 | F = A + B | Addition
0 | 0 | 1 | 1 | F = A + B + 1 | Add with carry
0 | 1 | 0 | 0 | F = A – B – 1 | Subtract with borrow
0 | 1 | 0 | 1 | F = A – B | Subtraction
0 | 1 | 1 | 0 | F = A – 1 | Decrement A
0 | 1 | 1 | 1 | F = A | Transfer A
1 | 0 | 0 | X | F = A + B | OR
1 | 0 | 1 | X | F = A B | XOR
1 | 1 | 0 | X | F = A . B | AND
1 | 1 | 1 | X | F = A’ | Complement A
Selection |  |  |  | Output | Function
S2 | S1 | S0 | Cin |  | 
0 | 0 | 0 | 0 | F = A | Transfer A
0 | 0 | 0 | 1 | F = A + 1 | Increment A
0 | 0 | 1 | 0 | F = A + B | Addition
0 | 0 | 1 | 1 | F = A + B + 1 | Add with carry
0 | 1 | 0 | 0 | F = A – B – 1 | Subtract with borrow
0 | 1 | 0 | 1 | F = A – B | Subtraction
0 | 1 | 1 | 0 | F = A – 1 | Decrement A
0 | 1 | 1 | 1 | F = A | Transfer A
1 | 0 | 0 | X | F = A + B | OR
1 | 0 | 1 | X |  | XOR
1 | 1 | 0 | X | F = A . B | AND
1 | 1 | 1 | X | F = A’ | Complement A