## Slide 1: (Prof.) D.K.MEHTA, ASSISTANT PROFESSOR,
CHEMICAL ENGINEERING DEPARTMENT,
L.E.COLLEGE-MORBI

## Slide 2
TOPIC:- CRYSTALLISATION
SUBJECT:-Mass Transfer Operation-I
SUBJECT CODE:-3150501

## Slide 3: Crystallization Principles
Crystallization is the formation of solid particles within a homogeneous phase.
Crystallization wide use has a twofold basis : (1) a crystal formed from an impure solution is itself pure (unless mixed crystals occur) (2) crystallization affords a practical method of obtaining pure chemical substances in a satisfactory condition for packaging and storing.

## Slide 4: Crystallization Principles
Magma:- In industrial crystallization from solution, the two-phase mixture of mother liquor and crystals of all sizes, which occupies the crystallizer and is withdrawn as product, is called a magma.
In practice, much of the retained mother liquor is separated from the crystals by filtration or centrifuging and the balance is removed by washing with fresh solvent. The effectiveness of these purification steps depends on the size and uniformity of the crystals.

## Slide 5: Importance of crystal size
Good yield and high purity are important objectives in crystallization, but the appearance and size range of a crystalline product also are significant.
If the crystals are to be marketed as a final product, customer acceptance requires individual crystals to be strong, non aggregated, uniform in size, and noncaking in the package.
For these reasons, crystal size distribution must be under control; it is a prime objective in the design and operation of crystallizers.

## Slide 6: Equilibria
Equilibrium in crystallization processes is reached when the solution is saturated, and the equilibrium relationship for bulk crystals is the solubility curve.
The solubility of extremely small crystal is greater than that of crystals of ordinary size.
Curves showing solubility as a function of temperature are given in Figure shown in next slide.

## Slide 7: Equilibria

## Slide 8: Equilibria
Most materials follow curves similar to curve 1 for KNO3; that is, their solubility increases more or less rapidly with temperature.
A few substances follow curves like curve 2 for NaCl, with little change in solubility with temperature.
Others follow curve 3 for MnSO4.H2O which is called an inverted solubility curve, which means that their solubility decreases as the temperature is raised.

## Slide 9: Supersaturation
In the formation of a crystal two steps are required :
(1) the birth of a new particle which as known as nucleation.
(2) crystal growth to microscopic size.
The driving potential for rates of both is supersaturation.
Supersaturation is the concentration difference between that of the supersaturated solution in which the crystal is growing and that of a solution in equilibrium with the crystal.

## Slide 10: Method to generate supersaturation
(1) Cooling (2)Evaporation (3) Salting (4) Precipitation
(1) Cooling:- If the solubility of the solute increases strongly with increase in temperature, as is the case with many common inorganic salts and organic substances, a saturated solution becomes supersaturated by simple cooling and temperature reduction.

## Slide 11: Method to generate supersaturation
(2)Evaporation:- If the solubility of the solute is relatively independent of temperature, as is the case with common salt, supersaturation may be generated by evaporating a portion of the solvent.
(3) Salting:- If neither cooling nor evaporation is desirable, as when the solubility is very high, supersaturation may be generated by adding a third component. The third component may act physically, with the original solvent, a mixed solvent in which the solubility of the solute is sharply reduced. This process is called salting.

## Slide 12: Method to generate supersaturation
(4) Precipitation:- If nearly complete precipitation is required, a new solute may be created chemically by adding a third component that will react with the original solute and form an insoluble substance. This process is called precipitation.

## Slide 13: Nucleation
The rate of nucleation is the number of new particles formed per unit time per unit volume of magma or solids-free mother liquor.
Nucleation refers to the birth of very small bodies of a new phase within a supersaturated homogeneous existing phase.
Nucleation is a consequence of rapid local fluctuations on a molecular scale in a homogeneous phase that is in a state of metastable equilibrium.

## Slide 14: Primary nucleation
The basic phenomenon is called homogeneous nucleation, which is further restricted to the formation of new particles within a phase uninfluenced in any way by solids of any sort, including the walls of the container or even the most minute particles of foreign substances.
When solid particles of foreign substances do influence the nucleation process by catalyzing an increase of nucleation rate at a given supersaturation or giving a finite rate at a supersaturation where homogeneous nucleation would occur only after a vast time. This is called heterogeneous nucleation.

## Slide 15: Homogeneous nucleation
In crystallization from solution, homogeneous nucleation almost never happens, except perhaps in some precipitation reactions.
Crystal nuclei may form from molecules, atoms or ions.
Because of their random motion, in any small volume several of these particles may associate to form what is called a cluster.
A cluster is a loose aggregation which usually disappears quickly. Occasionally enough particles associate into what is known as an embryo.

## Slide 16: Homogeneous nucleation
In embryo, there are the beginnings of a lattice arrangement and the formation of a new and separate phase.
For the most part, embryos have shot lives and revert to clusters or individual particles.
If supersaturation is large enough, an embryo may grow to such a size that it is in thermodynamic equilibrium with the solution, which is known as nucleus.

## Slide 17: Homogeneous nucleation
Nucleus Is the smallest assemblage of particles that will not redissolve and grow to form a crystals.
Few to several hundred particles are needed for stable nucleus. For water this number is 80.
Cluster embryo nucleus crystals

## Slide 18: Crystal growth
Crystal growth is a diffusional process, modified by the effect of the solid surfaces on which the growth occurs. Solute molecules or ions reach the growing faces of a crystal by diffusion through the liquid phase. The usual mass-transfer coefficient ky applies to this step.
On reaching the surface, the molecules or ion must be accepted by the crystal and organized into the space lattice. The reaction occurs at the surface at a finite rate.
Neither the diffusional nor the interfacial step will proceed unless the solution is supersaturated.

## Slide 19: Caking of crystals
When crystals are improperly stored cake or clumps of crystal are formed and it is known as caking of crystals.
Factors affecting caking:-
Shape and Size of crystals.
Melting point of crystals.
Impurities in crystals.
Humidity
Temperature fluctuations
Time of exposure

## Slide 20: Prevention of caking
Crystal must be more spherical.
Crystals must be of large size, more void and must be of narrow size distribution.
Crystals must have highest possible humidity.
Crystals must be covered with powdery inert material to prevent absorption of moisture e.g., table salt is coated with magnesia or tricalcium phosphate.

## Slide 21: Example
A solution consisting of 30% MgSO4 and 70% H2O is cooled at 150C. During cooling, 5% of the total water in the system evaporates. Concentration of mother liquor is 24.5% anhydrous MgSO4 and 75.5% H2O. How many kilograms of MgSO4 .7H2O crystals are obtained per 1000 kg of original mixture?

## Slide 22: Example

## Slide 23: Example

## Slide 24: Yields
In many industrial crystallization processes, the crystals and mother liquor are in contact long enough to reach equilibrium, and the mother liquor is saturated at the final temperature of the process.
The yield of the process can then be calculated from the concentration of the original solution and the solubility at the final temperature. If appreciable evaporation occurs during the process, this must be known or estimated.

## Slide 25: Yields
When the rate of crystal growth is slow, considerable time is required to reach equilibrium. this is especially true when the solution is viscous or where the crystals collect in the bottom of the crystallizer so there is little crystal surface exposed to the supersaturated solution. In such situations, the final mother liquor may retain appreciable supersaturation, and the actual yield will be less than that calculated form the solubility curve.
If the crystals are anhydrous, calculation of the yield is simple, as the solid phase contains no solvent.

## Slide 26: Crystallization Equipment
Commercial crystallizers may operate either continuously or batch wise. Except for special applications, continuous operation is preferred.
The first requirement of any crystallizer is to create a supersaturated solution, because crystallization cannot occur without supersaturation.

## Slide 27: Crystallization Equipment
Three methods are used to produce supersaturation.
(1) solutes like potassium nitrate and sodium sulfite are much less soluble at low temperatures than at high temperatures, so supersaturation can be produced simple by cooling.
(2) When the solubility is almost independent of temperature, as with common salt or reduces as the temperature is raised, supersaturation is developed by evaporation.
(3) In intermediate cases a combination of evaporation and cooling without evaporation, evaporation without cooling, or a combination of both.

## Slide 28: Continuous Vacuum crystallizer

## Slide 29: Continuous Vacuum Crystallizers
Most modern crystallizers fall in the category of vacuum units fin which adiabatic evaporative cooling is used to create supersaturation.
Continuous vacuum crystallizer with the conventional auxiliary units for feeding the unit and processing the product magma.
The magma circulates from the cone bottom of the crystallizer body through a downpipe to a low-speed low-head circulating pump, passes upward through a vertical tubular heater with condensing steam in the shell, and thence into the body.

## Slide 30: Continuous Vacuum Crystallizers
The heated stream enters through a tangential inlet just below the level of the magma surface. This imparts a swirling motion to the magma, which facilitates flash evaporation and equilibrates the magma with the vapor through the action of an adiabatic flash.
The supersaturation thus generated provides the driving potential for nucleation and growth.

## Slide 31: Continuous Vacuum Crystallizers
Feed solution enters the downpipe before the suction of the circulating pump.
Mother liquor and crystals are drawn off through a discharge pipe upstream from the feed inlet in the downpipe.
Mother liquor is separated from the crystals in a continuous centrifuge recycled to the downpipe.
The crystals are taken off as a product or for further processing.

## Slide 32: Draft tube-baffle crystallizer

## Slide 33: Draft tube-baffle crystallizer
The crystallizer body is equipped with a draft tube, which also acts as a baffle to control the circulation of the magma, and an upward-directed propeller agitator to provide a controllable circulation within the crystallizer.
An additional circulation system, outside the crystallizer body and driven by a circulating pump, contains the heater and feed inlet.
Product slurry is removed through an outlet near the bottom of the conical lower section of the crystallizer body.

## Slide 34: Draft tube-baffle crystallizer
For a given feed rate, both the internal and external circulations are independently variable and provide controllable variables for obtaining the required CSD ( Crystal Size Distribution).
It may have elutriation leg below the body to classify the crystals by size and may also be equipped with a baffled settling zone for fines removal.
Part of the circulating liquor is pumped to the bottom of the leg and used as a hydraulic sorting fluid to carry small crystals back into the crystallizing zone for further growth.

## Slide 35: Draft tube-baffle crystallizer
The discharge slurry is withdrawn from the lower part of the elutriation leg and sent to a filter or centrifuge, and the mother liquor is returned to the crystallizer.
Unwanted nuclei are removed by providing an annular space or jacket.
This annular space provides a settling zone, in which hydraulic classification separates fine crystals from larger ones by floating them in an upward-flowing stream of mother liquor, which is withdrawn from the top of the settling zone.

## Slide 36: Swenson walker crystallizer

## Slide 37: Swenson walker crystallizer
It is continuous type crystallizer.
It works on principle of supersaturation by cooling.
It consists of U-shaped open trough with a semi cylindrical bottom.
A water jacket is welded to the outside of trough. This jacket is divided into section so that differential cooling may be used in various zones.

## Slide 38: Swenson walker crystallizer
A slow speed, long pitch spiral blade agitator is set as close to the trough as possible.
Feed is entered at one end of trough and cooling water flows through other end.
Nucleation start by short cold zone followed by gradual cooling.
Spiral stirrer prevents accumulation of crystals on the cooing surface. It lifts crystals and shower them down through the solution so crystal grow uniformly and free from aggregates and inclusion of mother liquor.

## Slide 39: Swenson walker crystallizer
At the end of crystallizer there is overflow gate where crystals and mother liquor overflow to drain box.
From the mixture, mother liquor is returned to the process and wet crystals are fed to the centrifuge.
This crystallizer requires less floor space and labor and gives uniform size crystals.

## Slide 40: Application of crystallization
It is used to get pure salt from sea water.
To obtain alum crystals from impure alum.
Purification of drugs.
To produce drugs in different crystal form used in the production of certain sustained release dosage forms.
Production of sugar from sugar beet.