## Slide 1
KINEMATICS OF MACHINES (KOM)
L. E. College, Morbi-2
Industrial Engineering Department
Chapter-02–Velocity and Acceleration Analysis of Mechanisms:
Prepared by Prof. Divyesh B. Patel
Mechanical Engg. Dept
LE. College, Morbi
+919925282644
divyesh21dragon@gmail.com

## Slide 2: A mechanism of a crank and slotted lever quick return motion is shown in Fig. If the crank rotates counter clockwise at 120 r.p.m., determine for the configuration shown, the velocity and acceleration of the ram D. Also determine the angular acceleration of the slotted lever. Crank, AB = 150 mm ; Slotted arm, OC = 700 mm and link CD = 200 mm
O
A
B’
B
C
D
450
300
400
Prepared by Prof. D.B.Patel
Mechanical Engg. Dept
LE. College, Morbi

## Slide 3
O
A
B’
B
C
D
450
300
400
NBA= 120 rpm
ωBA =2 N/60 = 2 120/60 =12.57 rad/sec
vBA = ωBA ×AB = 12.57 × 0.15 = 1.9 m/s
Space Diagram
vBA
Velocity Diagram
a,o
b
vB’O
b’
ob’ / oc = OB’ / OC
oc = OC/OB’ ×ob’
c
d
ωOC = ωOB’ = vCO /OC
ωOC = 3.07 rad/sec
Prepared by Prof. D.B.Patel
Mechanical Engg. Dept
LE. College, Morbi

## Slide 4
O
A
B’
B
C
D
450
300
400
Space Diagram
vBA
vB’O
a’,o’
b’
arBA
aCBB’
We know that radial component of the acceleration of B with respect to A,
arBA = ω2BA × AB = (12.57)2 × 0.15 = 23.7 m/s2
Coriolis component of the acceleration of slider B with respect to the coincident point B',
aCBB’ = 2ωCO ×vBB’ = 2 × 3.07 × 1.05= 6.45 m/s2
arBB’
x’
y’
arB’O
atB’O
b’’
o’b’’ / o’c’ = OB’ / OC
o’c’ = OC/OB’ ×o’b’’
c’
aBB’
arDC
atDC
d’
We know that radial component of the acceleration of B’ with respect to O,
arB’O = V2B’O /BO’= (1.55)2/0.52 = 4.62 m/s2
We know that radial component of the acceleration of D with respect to C,
arDC = V2DC /DC= (0.45)2/0.2 = 1.01 m/s2
Prepared by Prof. D.B.Patel
Mechanical Engg. Dept
LE. College, Morbi

## Slide 5: In a Whitworth quick return motion, as shown in Fig. OA is a crank rotating at 30 r.p.m. in a clockwise direction. The dimensions of various links are : OA = 150 mm; OC = 100 mm; CD = 125 mm; and DR = 500 mm. Determine the acceleration of the sliding block R and the angular acceleration of the slotted lever CA.
O
A
B
C
D
450
100
500
R
Prepared by Prof. D.B.Patel
Mechanical Engg. Dept
LE. College, Morbi

## Slide 6
O
A
B
C
D
450
NAO= 30 rpm
ωAO =2 N/60 = 2 × 30/60 =3.142 rad/sec
vAO = ωAO ×AO = 3.142 × 0.15 = 0.47 m/s
vAO
Velocity Diagram
c,o
a
b
d
r
R
cb / bd = CB / BD or
bd = (BD/CB)×cd
vAB
vBC
ωBC = ωCD = vBC /CB
ωBC = 1.92 rad/sec
vDR
Prepared by Prof. D.B.Patel
Mechanical Engg. Dept
LE. College, Morbi

## Slide 7
O
A
B
C
D
450
vAO
c’,o’
a’
x
b’
d’
R
We know that radial component of the acceleration of A with respect to O
arAO = ω2AO × OA = (3.142)2 × 0.15 = 1.47 m/s2
Coriolis component of the acceleration of slider A with respect to the coincident point B,
aCAB = 2ωBC ×vAB = 2 × 1.92 × 0.15= 0.576 m/s2
aCAB
arAB
We know that radial component of the acceleration of B with respect to C,
arBC = V2BC /BC= (0.46)2/0.24 = 0.88 m/s2
arBC
y
atBC
c’b’ / b’d’ = CB / BD
b’d’ = (BD/CB)×c’d’
We know that radial component of the acceleration of R with respect to D,
arRD = V2RD /DR= (0.12)2/0.5 = 0.029 m/s2
z
arRD
atRD
r’
aR
αBC= atBC / BC
αBC = 0.14/ 0.24
= 0.583 rad/s2

## Slide 8
Thank you