## Slide 1
Sequential circuit

## Slide 2: Topics to be covered
Flip-flops
Applications of Flip-flops
Shift registers
Asynchronous counters
Synchronous counters
Sequential counters

## Slide 3: Sequential Switching Circuits
Sequential switching circuits are circuits whose output levels at any instant of time are dependent on the levels present at the inputs at that time and on the state of the circuit, i.e., on the prior input level conditions (i.e. on its past inputs)
The past history is provided by feedback from the output back to the input.
Made up of combinational circuits and memory elements.
Eg. Counters, shift registers, serial adder, etc.

## Slide 4: Sequential Switching Circuits
Combinational Circuit
Memory elements
Inputs
Outputs

## Slide 5: Sequential Circuits v/s Combinational Circuits
Sequential Circuits
In sequential circuits, the output variables at any instant of time are dependent on the present input variables and on the present state, i.e., on the past history of the system.
Memory unit is required to store the past history of the input variables in sequential circuits.
Sequential circuits are slower than combinational circuits.
Sequential circuits are comparatively harder to design.
Combinational Circuits
In combinational circuits, the output variables at any instant of time are dependent only on the present input variables.
Memory unit is not required in combinational circuits.
Combinational circuits are faster because the delay between the input and the output is due to propagation delay of gates only.
Combinational circuits are easy to design.

## Slide 6: Flip-flop
A flip-flop, known formally as bistable multivibrator, has two stable states.
It can remain in either of the states indefinitely.
Its state can be changed by applying the proper triggering signal.

## Slide 7: Latch
Latch is used for certain flip-flop which are non-clocked.
These flip-flops ‘latch on’ to a 1 or a 0 immediately upon receiving the input pulse called SET or RESET.

## Slide 8: S-R Flip-Flop (Latch)
The simplest type of flip-flop is called an S-R latch.
It has two outputs labelled Q and Q’ and two inputs labelled S and R. The state of the latch corresponds to the level of Q (HIGH or LOW, 1 or 0) and Q’ is the complement of that state.
It can be constructed using either two cross-coupled NAND gates or two-cross coupled NOR gates.
Using two NOR gates, an active-HIGH S-R latch can be constructed and using two NAND gates an active-LOW S-R latch can be constructed.
The name of the latch, S-R or SET-RESET, is derived from the names of its inputs.

## Slide 9: NOR Gate S-R latch (Active High)
S
R
Q
Q’
Inputs
Outputs
S | R | Qn | Qn+1 | State
0 0 | 0 0 | 0 1 | 0 1 | No Change
0 0 | 1 1 | 0 1 | 0 0 | Reset
1 1 | 0 0 | 0 1 | 1 1 | Set
1 1 | 1 1 | 0 1 | x x | Indeterminate (invalid)
R
S
Q
Q’
Logic diagram
Logic Symbol

## Slide 10: NAND Gate S-R latch (Active Low)
S | R | Qn | Qn+1 | State
0 0 | 0 0 | 0 1 | x x | Indeterminate (invalid)
0 0 | 1 1 | 0 1 | 1 1 | Set
1 1 | 0 0 | 0 1 | 0 0 | Reset
1 1 | 1 1 | 0 1 | 0 1 | No Change
S
R
Q
Q’
Logic diagram

## Slide 11: Gated S-R Latch (S-R Flip flop)
S
R
Q
Q’
EN | S | R | Qn | Qn+1 | State
1 1 | 0 0 | 0 0 | 0 1 | 0 1 | No Change
1 1 | 0 0 | 1 1 | 0 1 | 0 0 | Reset
1 1 | 1 1 | 0 0 | 0 1 | 1 1 | Set
1 1 | 1 1 | 1 1 | 0 1 | x x | Indeterminate (invalid)
0 0 | x x | x x | 0 1 | 0 1 | No Change
S
R
Q
Q’
Logic diagram
Logic Symbol
EN
EN

## Slide 12: Gated D-Latch
D
Q
Q’
EN | D | Qn | Qn+1 | State
1 1 | 0 0 | 0 1 | 0 0 | Reset
1 1 | 1 1 | 0 1 | 1 1 | Set
0 0 | x x | 0 1 | 0 1 | No Change
D
Q
Q’
Logic diagram
Logic Symbol
EN
EN
What if shot both input of SR and put NOT gate at one input
New flip flop is generated D- flip flop.
Input will be given as output.
D Mean Data.
Also called Buffer flip flop.

## Slide 13: J-K Flip-Flop
J
K
Q
Q’
Logic Symbol
EN
J
K
Q
Q’
EN
EN | J | K | Qn | Qn+1 | State
1 1 | 0 0 | 0 0 | 0 1 | 0 1 | No Change
1 1 | 0 0 | 1 1 | 0 1 | 0 0 | Reset
1 1 | 1 1 | 0 0 | 0 1 | 1 1 | Set
1 1 | 1 1 | 1 1 | 0 1 | 1 0 | Toggle
0 0 | x x | x x | 0 1 | 0 1 | No Change
Invalid state of SR flip flop is corrected.
New flip flop is JK flip flop.
All other functionalities are same.

## Slide 14: T Flip-Flop
T
Q
Q’
Logic Symbol
EN
T
Q
EN
Q’
EN | T | Qn | Qn+1 | State
1 1 | 0 0 | 0 1 | 0 1 | No change
1 1 | 1 1 | 0 1 | 1 0 | Toggle
0 0 | x x | 0 1 | 0 1 | No Change
What If we shot both input of JK flip flop.
New flip flop is generated called Toggle flipflop.
Toggle = T
Here Output will toggle(from its previous) if input is given 1

## Slide 15: Application of Flip flops
Parallel Data Storage
  1 flip flop to store 1 bit => N flip flop to store N – bits data
  Data available at input of D-FF, on clock pulse data will be transferred to output Q.
  FF are connected parallelly.
Serial Data Storage
  FF are cascaded.
Transfer of Data
  Serially or parallelly
Serial to Parallel conversion
Parallel to serial conversion

## Slide 16: Application of Flip flops
Counting
  FF are connected in particular fashion to count pulses electronically called counters
  1 FF can count up to 2 pulses.
  2 FF can count up to pulses =>n FF count -
Frequency division
  FF are connected in particular fashion to divide input frequenct called ripple counter
  1 FF can be used to divide input frequency by 2
  2 FF can divide frequency by =>n FF can divide fr. By

## Slide 17: Registers (Group of FF)
As a flip-flop (FF) can store only one bit of data, a 0 or a 1, it is referred to as a single-bit register.
A register is a set of FFs used to store binary data.
The storage capacity of a register is the number of bits (1s and 0s) of digital data it can retain.

## Slide 18: Registers
Loading a register means setting or resetting the individual FFs, i.e. inputting data into the register so that their states correspond to the bits of data to be stored.
Loading may be serial or parallel.
In serial loading, data is transferred into the register in serial form i.e. one bit at a time.
In parallel loading, the data is transferred into the register in parallel form meaning that all the FFs are triggered into their new states at the same time.

## Slide 19: Types of Registers
Buffer register
Shift register
Bidirectional shift register
Universal shift register

## Slide 20: Buffer register
FF1
D1
Q1
>
FF2
D2
Q2
>
FF3
D3
Q3
>
FF4
D4
Q4
>
CLK
CLK
x1
x2
x3
x4
When clock pulse applied stored word Q becomes X
Q4Q3Q2Q1=X1X2X3X4 or Q=X

## Slide 21: Shift Register
A number of FFs connected together such that data may be shifted into and shifted out of them is called a shift register.
Data may be shifted into or out of the register either in serial form or in parallel form.
So, there are four basic types of shift registers:
  serial-in, serial-out
  serial-in, parallel out
  parallel-in, serial-out
  parallel-in, parallel-out
Data may be rotated left or right. Data may be shifted from left to right or right to left at will, i.e. in a bidirectional way.
Also, data may be shifted in serially (in either way) or in parallel and shifted out serially (in either way) or in parallel.

## Slide 22: Data transmission in shift register
Serial-in, serial-out shift-right, shift register
Serial data input
Serial data output
Serial-in, serial-out shift-left, shift register
Serial data output
Serial data input

## Slide 23: Data transmission in shift register
Serial-in, parallel-out, shift register
Serial data input
Parallel data output
Parallel-in, parallel-out, shift register
Parallel data input
Parallel data output

## Slide 24: Data transmission in shift register
Parallel-in, serial-out, shift register
Serial data output
Parallel data input

## Slide 25: Serial-in, Serial-out, Shift register
FF1
D1
Q1
>
FF2
D2
Q2
>
FF3
D3
Q3
>
FF4
D4
Q4
>
Serial Input
CLK
Serial output

## Slide 26: Serial-in, Serial-out, Shift register
CLK
Serial output
Using J-K Flip Flop
FF1
J1
Q1
>
K1
Q1’
FF2
J2
Q2
>
K2
Q2’
FF3
J3
Q3
>
K3
Q3’
FF4
J4
Q4
>
K4
Q4’
Serial input

## Slide 27: Serial-in, Serial-out, Shift-left, Shift register
FF4
Q4
D4
<
FF3
Q3
D3
<
FF2
Q2
D2
<
FF1
Q1
D1
<
Serial Output
CLK
Serial input

## Slide 28: Serial-in, Parallel-out, Shift register
FF1
D1
QA
>
FF2
D2
QB
>
FF3
D3
QC
>
FF4
D4
QD
>
Serial Input
CLK
QA
QB
QC
QD

## Slide 29: Parallel-in, Serial-out, Shift register
FF1
D1
Q1
>
FF2
D2
Q2
>
FF3
D3
Q3
>
FF4
D4
Q4
>
Shift/
CLK
A
B
C
D

## Slide 30: Parallel-in, Parallel-out, Shift register
FF1
D
Q
>
FF2
D
Q
>
FF3
D
Q
>
FF4
D
Q
>
A
CLK
B
C
D
QA
QB
QC
QD

## Slide 31: Counters
Synchronous counters and asynchronous counters
Asynchronous counter = ripple counters

## Slide 32: Asynchronous Counters v/s Synchronous Counters
Asynchronous Counters
Synchronous Counters
In this type of counters FFs are connected in such a way that the output of the first FF drives the clock for the second FF, the output of the second the clock of the third and so on.
All the FFs are not clocked simultaneously.
Design and implementation is very simple even for more number of states.
Main drawback of these counters is their low speed as the clock is propagated through a number of FFs before it reaches the last FF.
In this type of counters there is no connection between the output of first FF and clock input of next FF and so on.
All the FFs are clocked simultaneously.
Design and implementation becomes tedious and complex as the number of states increases.
Since clock is applied to all the FFs simultaneously the total propagation delay is equal to the propagation delay of only one FF. Hence they are faster.

## Slide 33: 2-bit Ripple Up-Counter using Negative Edge-triggered Flip-Flop
FF1
J1
Q1
>
K1
Q1’
FF2
J2
Q2
>
K2
Q2’
1
1
Q1
Q2
CLK
CLK | Present State |  | Next State | 
 | Q2 | Q1 | Q2 | Q1
 | 0 | 0 | 0 | 1
 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1
 | 1 | 1 | 0 | 0
CLK
Q1
Q2
0
1
0
1
0
0
1
0

## Slide 34: 2-bit Ripple Down-Counter using Negative Edge-triggered Flip-Flop
CLK | Present State |  | Next State | 
 | Q2 | Q1 | Q2 | Q1
 | 0 | 0 | 1 | 1
 | 1 | 1 | 1 | 0
 | 1 | 0 | 0 | 1
 | 0 | 1 | 0 | 0
FF1
J1
Q1
>
K1
Q1’
FF2
J2
Q2
>
K2
Q2’
1
1
Q1
Q2
CLK
CLK
Q1
Q2
0
1
0
1
0
0
1
0
Q1’
1
0
1
0
1

## Slide 35: 2-bit Ripple Up-Counter using Positive Edge-triggered Flip-Flop
FF1
J1
Q1
>
K1
Q1’
FF2
J2
Q2
>
K2
Q2’
1
1
Q1
Q2
CLK
CLK | Present State |  | Next State | 
 | Q2 | Q1 | Q2 | Q1
 | 0 | 0 | 0 | 1
 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1
 | 1 | 1 | 0 | 0
CLK
Q1
Q2
0
0
0
1
0
0
1
1
1
Q1’
1
1
1
0
0
0

## Slide 36: 2-bit Ripple Down-Counter using Positive Edge-triggered Flip-Flop
FF1
J1
Q1
>
K1
Q1’
FF2
J2
Q2
>
K2
Q2’
1
1
Q1
Q2
CLK
CLK | Present State |  | Next State | 
 | Q2 | Q1 | Q2 | Q1
 | 0 | 0 | 1 | 1
 | 1 | 1 | 1 | 0
 | 1 | 0 | 0 | 1
 | 0 | 1 | 0 | 0
CLK
Q1
Q2
0
0
0
1
0
0
1
1
1

## Slide 37: Ring Counter
FF1
D1
Q1
>
FF2
D2
Q2
>
FF3
D3
Q3
>
FF4
D4
Q4
>
CLK
Q1’
Q2’
Q3’
Q4’
FF1
J1
Q1
>
FF2
J2
Q2
>
FF3
J3
Q3
>
FF4
J4
Q4
>
CLK
Q1’
Q2’
Q3’
Q4’
K1
K2
K3
K4

## Slide 38: Ring Counter
After pulses | State |  |  | 
 | Q1 | Q2 | Q3 | Q4
0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0
2 | 0 | 0 | 1 | 0
3 | 0 | 0 | 0 | 1
4 | 1 | 0 | 0 | 0
5 | 0 | 1 | 0 | 0
6 | 0 | 0 | 1 | 0
7 | 0 | 0 | 0 | 1

## Slide 39: Mod-6 Asynchronous Counter
After pulses | State |  |  | Reset(R)
 | Q3 | Q2 | Q1 | 
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
2 | 0 | 1 | 0 | 0
3 | 0 | 1 | 1 | 0
4 | 1 | 0 | 0 | 0
5 | 1 | 0 | 1 | 0
6 | 1 | 1 | 0 | 1
 | ↓ | ↓ | ↓ | 
 | 0 | 0 | 0 | 0
 | 0 | 0 | 1 | 0
R = 0 for 000 to 101
R = 1 for 110
R = x for 111
R = Q3Q2Q1’ + Q3Q2Q1
R = Q3Q2

## Slide 40: Mod-6 Asynchronous Counter
FF1
T1
Q1
>
Q1’
FF2
T2
Q2
>
Q2’
FF3
T3
Q3
>
Q3’
1
Q1
Q2
1
1
Q3
R’
CLK

## Slide 41: Exercise
Design Mod-10 ripple counter.
Draw a frequency divider using JK FFs to divide input clock frequency by a factor of 8.

## Slide 42: Design of Synchronous Counters
Step 1. Number of flip-flops:
Based on the description of the problem, determine the required number n of the FFs - the smallest value of n is such that the number of states N ≤ 2n and the desired counting sequence.
Step 2. State diagram:
Draw the state diagram showing all the possible states.
Step 3. Choice of flip-flops and excitation table:
Select the type of flip-flops to be used and write the excitation table.
An excitation table is a table that lists the present state (PS), the next state (NS) and the required excitations.

## Slide 43: Design of Synchronous Counters
Step 4. Minimal expressions for excitations:
Obtain the minimal expressions for the excitations of the FFs using K-maps for the excitations of the flip-flops in terms of the present states and inputs.
Step 5. Logic Diagram:
Draw the logic diagram based on the minimal expressions.

## Slide 44: Excitation Tables
PS | NS | Required inputs | 
Qn | Qn+1 | S | R
0 | 0 | 0 | x
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | x | 0
S-R FF
PS | NS | Required inputs | 
Qn | Qn+1 | J | K
0 | 0 | 0 | x
0 | 1 | 1 | x
1 | 0 | x | 1
1 | 1 | x | 0
J-K FF

## Slide 45: Excitation Tables
PS | NS | Required inputs
Qn | Qn+1 | D
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
D FF
T FF
PS | NS | Required inputs
Qn | Qn+1 | T
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 46: Design of Synchronous 3-bit Up Counters
Step 1. Number of flip-flops:
A 3-bit up-counter requires 3 flip-flops. The counting sequence is 000, 001, 010, 011, 100, 101, 110, 111, 000 …
Step 2. Draw the state diagram:
000
001
010
011
100
101
110
111

## Slide 47: Design of Synchronous 3-bit Up Counters
Step 3. Select the type of flip-flops and draw the excitation table:
JK flip-flops are selected and the excitation table of a 3-bit up-counter using J-K flip-flops is drawn as shown below.
PS |  |  | NS |  |  | Required excitations |  |  |  |  | 
Q3 | Q2 | Q1 | Q3 | Q2 | Q1 | J3 | K3 | J2 | K2 | J1 | K1
0 | 0 | 0 | 0 | 0 | 1 | 0 | x | 0 | x | 1 | x
0 | 0 | 1 | 0 | 1 | 0 | 0 | x | 1 | x | x | 1
0 | 1 | 0 | 0 | 1 | 1 | 0 | x | x | 0 | 1 | x
0 | 1 | 1 | 1 | 0 | 0 | 1 | x | x | 1 | x | 1
1 | 0 | 0 | 1 | 0 | 1 | x | 0 | 0 | x | 1 | x
1 | 0 | 1 | 1 | 1 | 0 | x | 0 | 1 | x | x | 1
1 | 1 | 0 | 1 | 1 | 1 | x | 0 | x | 0 | 1 | x
1 | 1 | 1 | 0 | 0 | 0 | x | 1 | x | 1 | x | 1

## Slide 48: Design of Synchronous 3-bit Up Counters
Step 4. Obtain the minimal expressions
From excitation table, J1 = K1 = 1.
K – Maps for excitations J3, K3, J2 and K2 and their minimized form are as follows:
Q3Q2
Q1
00
10
0
1
01
11
1
x
x
x
x
J3 = Q2Q1
Q3Q2
Q1
00
10
0
1
01
11
1
x
x
x
x
K3 = Q2Q1

## Slide 49: Design of Synchronous 3-bit Up Counters
Q3Q2
Q1
00
10
0
1
01
11
1
x
1
x
J2 = Q1
Q3Q2
Q1
00
10
0
1
01
11
1
x
x
x
x
K2 = Q1
1
x
x

## Slide 50: Design of Synchronous 3-bit Up Counters
Step 5. Draw the logic diagram
FF1
J1
Q1
>
K1
Q1’
FF2
J2
Q2
>
K2
Q2’
1
FF3
J3
Q3
>
K3
Q3’
CLK

## Slide 51: Sequence Generator (Pulse Train Generators)
Using Direct logic
Inspect given pulse train
Decide the number of unique states and minimum number of FFs required.
If unique states are not possible with the least number of FFs n, then increase the number of FFs by one or more to get the unique states.

## Slide 52: Sequence Generator (Direct Logic)
0
1
1
1
0
1
1
1
0
FF States | 
 | LSB
0 | 0
0 | 1
1 | 1
? | 1
FF States |  |  | Decimal equivalent
 |  | LSB | 
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 1 | 3
1 | 0 | 1 | 5
0
1
3
5
State assignment
State diagram
Example: Generate the following pulse train using direct logic.

## Slide 53: Sequence Generator (Direct Logic)
PS |  |  | NS |  |  | Required excitations |  |  |  |  | 
Q3 | Q2 | Q1 | Q3 | Q2 | Q1 | J3 | K3 | J2 | K2 | J1 | K1
0 | 0 | 0 | 0 | 0 | 1 | 0 | X | 0 | X | 1 | X
0 | 0 | 1 | 0 | 1 | 1 | 0 | X | 1 | X | X | 0
0 | 1 | 1 | 1 | 0 | 1 | 1 | X | X | 1 | X | 0
1 | 0 | 1 | 0 | 0 | 0 | X | 1 | 0 | X | X | 1
J3 = Q2
K3 = 1
J2 = Q3’Q1
K2 = 1
J1 = 1
K1 = Q3

## Slide 54: Sequence Generator (Direct Logic)
FF1
J1
Q1
>
K1
Q1’
FF2
J2
Q2
>
K2
Q2’
1
CLK
FF2
J3
Q3
>
K3
Q3’
1
1

## Slide 55: Sequence Generator (Indirect Logic)
Example: Generate the following pulse train using indirect logic.
0
1
1
0
1
0
1
1
0
1
1
Q3 | Q2 | Q1 | Output(f) | States
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 2
0 | 1 | 1 | 1 | 3
1 | 0 | 0 | 0 | 4
1 | 0 | 1 | X | 5
1 | 1 | 0 | X | 6
1 | 1 | 1 | X | 7
Q3Q2
Q1
00
10
0
1
01
11
1
x
x
x
f = Q2 + Q3’ Q1’
1
1

## Slide 56: Sequence Generator (Indirect Logic)
FF1
J1
Q1
>
K1
Q1’
FF2
J2
Q2
>
K2
Q2’
FF2
J3
Q3
>
K3
Q3’
1
1
1
CLK
f