## Slide 1
BASIC MECHANICAL ENGINEERING (BME)
L. E. College, Morbi-2
Mechanical Engineering Department
Chapter– I.C. Engine
Prepared by Prof. Divyesh B. Patel
Mechanical Engg. Dept
LE. College, Morbi
+919925282644
divyesh21dragon@gmail.com

## Slide 2
Comparison between I.C. and E.C. Engine
1 | Combustion of fuel takes place inside the engine cylinder | Combustion of fuel takes place outside the engine cylinder
Sr. No. | Internal combustion Engine | External combustion Engine
2 | Working fluid is the products of air-fuel mixture | Working fluid is steam.
3 | Thermal efficiency is higher (30-35 %) | Thermal efficiency is lower (15-25 %)
5 | Fuel used are petrol, diesel and gas which are costlier. | Coal is used as fuel which is cheaper.
4 | Power developed per kg of weight of engine is higher. | Power developed per kg of weight of engine is lower.
6 | It can be quickly started. | It requires more time for starting as steam has to be generated in boiler.
7 | Initial cost is low | Initial cost is low
8 | Absence of heat exchangers and boiler results in mechanical simplicity. | Due to presence of heat exchangers and boiler. It is comparatively complex in construction.
9 | Small capacity power generation. | High capacity power generation.
10 | Working pressure and temperature are higher, so components are to be made more heat resistant. | Working pressure and temperature are comparatively lower.
11 | Product of combustion after doing work are exhausted to atmosphere. | Steam is condensed and fed back to the boiler. Same working fluid is used again.
12 | Examples are petrol engine, diesel engine and open cycle gas turbine. | Examples are steam engine, steam turbine and close cycle gas turbine.
Prepared by Prof. D.B.Patel
Mechanical Engg. Dept
LE. College, Morbi

## Slide 3
Classification of I.C. Engines
Type of Fuel used :
Number of strokes Required to complete the cycle:
Cycle of operation:
Method of ignition:
Method of Cooling:
Method of Governing:
Speed of engine:
Number of cylinder:
Arrangement of cylinder:
Fuel supply system:
Lubrication system:
Location of valves:
Application:
i ) Petrol ii) Diesel iii) Gas engine iv) Bi-fuel
i) Four stroke engine ii) Two stroke engine
i ) Otto cycle or constant volume cycle ii) Diesel cycle or pressure volume cycle iii) Dual cycle or semi-diesel cycle
i) Spark ignition ii) Compression ignition
i) Air cooling ii) Water cooling
i) Quantity governor ii) Quality governor
i) Low speed ii) Medium speed iii) High speed
i) Single cylinder ii) Multi cylinder
i) Carburetor ii) Injector
i) Horizontal engine ii) Vertical engine iii) V-type engine iv) Redial engine v) Opposed piston engine v) Opposed Cylinder engine
i) Splash lubrication ii) Pressure lubrication system
i) Overhead valve engine ii) Side valve engine
Prepared by Prof. D.B.Patel
Mechanical Engg. Dept
LE. College, Morbi

## Slide 4
I.C. Engine parts and their function
Frame:
Bed Plate
Crankcase
Lubricating oil
Cylinder:
Piston
Water jacket
Cylinder Head:
Inlet valve
Exhaust valve
Spark plug or Injector
Piston:
Piston Ring:
Piston rings
Piston Pin or Gudgeon Pin:
Piston Pin
Connecting rod:
Connecting rod
Crankshaft
Crankshaft
Valves
Camshaft
Camshaft
Cam
Cam
Push rod & rocker arm
Push rod
Rocker arm
Flywheel
Fuel pump

## Slide 5
Important terms used in I.C. Engines
Bore (D)
Stroke (L)
D
Stroke (L)
Dead Centres
Top dead Centres (TDC) & bottom dead centre (BDC)
Piston
T.D.C.
B.D.C.
Inner dead Centres (IDC) & Outer dead centre (ODC)
D
Stroke (L) =D
I.D.C.
O.D.C.
Clearance Volume (VC)
Swept or stroke Volume (VS)
Compression ratio
Piston Speed
Prepared by Prof. D.B.Patel
Mechanical Engg. Dept
LE. College, Morbi

## Slide 6
Working of four stroke Petrol engine
Definition:
Suction Stroke:
P
V
1
2
3
4
Clearance volume
Swept volume
Total volume
0
Compression Stroke:
Atm. pressure
Expansion or power Stroke:
Exhaust Stroke:
Suction
Exhaust
TDC
BDC
Prepared by Prof. D.B.Patel
Mechanical Engg. Dept
LE. College, Morbi

## Slide 7
Working of four stroke Diesel engine
Definition:
Suction Stroke:
P
V
1
2
3
4
Clearance volume
Swept volume
Total volume
0
Compression Stroke:
Atm. pressure
Expansion or power Stroke:
Exhaust Stroke:
Suction
Exhaust
TDC
BDC
Prepared by Prof. D.B.Patel
Mechanical Engg. Dept
LE. College, Morbi

## Slide 8
Working of Two stroke Petrol engine
First Stroke
Second Stroke
Where E = Exit Port
I = Inlet Port
T = Transfer Port
TDC
BDC
scavenging
Mixture of air-fuel
Spark plug
Mixture of air-fuel
Prepared by Prof. D.B.Patel
Mechanical Engg. Dept
LE. College, Morbi

## Slide 9
Working of Two stroke Diesel engine
First Stroke
Second Stroke
Where E = Exit Port
I = Inlet Port
T = Transfer Port
TDC
BDC
scavenging
Only air
Injector
Air
Prepared by Prof. D.B.Patel
Mechanical Engg. Dept
LE. College, Morbi

## Slide 10
Comparison between Petrol and Diesel Engine
1 | Basic Cycle | Otto Cycle | Diesel Cycle
Sr. No. | Parameter | S.I Engine | C.I Engine
2 | Fuel | Petrol | Diesel
4 | Ignition | Spark plug is used to ignite the fuel-air mixture | The temperature at the end of compression stroke is sufficient to ignite the fuel.
3 | Introduction of Fuel | A mixture of fuel and air is introduced in the cylinder during suction stroke. | Fuel is injected directly into the combustion chamber using pump and injector.
5 | Compression ratio | 6 to 10 | 14 to 22
6 | Speed | They are high speed engines due to light weight. | The are low speed engines due to heavy weight.
7 | Thermal efficiency | Due to use of low compression ratio thermal efficiency is low | Due to use of high compression ratio thermal efficiency is high.
8 | Weight | They are light in weight due to use of lower peak ratio pressure. | They are heavy in weight due to use of high peak ratio pressure.
9 | Initial and Maintance cost | Low | High
10 | Governor | Quantity governor method is used for controlling the speed. | Quality governor method is used for controlling the speed.
11 | Vibration and Noise | Lower due to use of lower cylinder pressure | Higher due to use of lower cylinder pressure
12 | Application | Employed for light duty vehicles | Employed for heavy duty vehicles
Prepared by Prof. D.B.Patel
Mechanical Engg. Dept
LE. College, Morbi

## Slide 11
Comparison between Four stroke and Two stroke Engine
1 | Number of strokes and revolution | Cycle is completed in four strokes of the piston or in two revolution of the crank | Cycle is completed in two strokes of the piston or one revolution of the crankshaft.
Sr. No. | Parameter | Four stroke Engine | Two stroke Engine
2 | Number of power strokes | It has one power stroke for every two revolution. | It has one power stroke for each revolution of crankshaft. So theoretically power devolved is twice that of four stroke engine.
4 | Admission of charge | Charge is directly admitted into the engine cylinder during suction stroke. | Charge is first admitted into the crankcase and then transferred to the engine cylinder.
3 | Weight and space requirement | Engine is heavy and bulky. It occupies more space. | Engine is light and bulky. It occupies less space.
5 | Construction | Construction is complicated due to presence of valve and valve gear mechanism. | Construction is simple due to absence of valve and valve gear mechanism.
6 | Thermal efficiency | Higher thermal efficiency as there is no mixing of fresh charge with exhaust gases. | Lower thermal efficiency as there is mixing of fresh charge with exhaust gases and some fuel leaves along with exhaust gases without burning.
7 | Cooling and lubrication requirement | Lesser cooling and lubrication needed since it has only one power stroke per two revolution of crankshaft. | More cooling and lubrication needed since it has only one power stroke per revolution of crankshaft.
8 | Lubrication system | They have separate lubrication system. | Lubricating oil is mixed with petrol in two stroke petrol engine and admitted into the engine
9 | Mechanical efficiency | It is low due to more number of parts. | It is high due to less number of parts.
Prepared by Prof. D.B.Patel
Mechanical Engg. Dept
LE. College, Morbi

## Slide 12
Performance Parameters
Indicated Power (IP)
Where Pm = Indicated mean effective Pressure (N/m2)
L =Stroke Length (m)
n = Number of working strokes per minute
n=N/2 (For Four stroke) =N (Two stroke)
Break Power (IP)
Where Pmb = Indicated mean effective Pressure (N/m2)
T = Torque (N-m)
L =Stroke Length (m)
N = Speed of Engine (rpm)
Prepared by Prof. D.B.Patel
Mechanical Engg. Dept
LE. College, Morbi

## Slide 13
Performance Parameters
Break Power (IP)
Measurement of break power by rope break dynamometer
Let W = Dead weight (N)
S = Spring balance (N)
Rm =Mean effective radius (m)
D = Drum or Pully diameter (m)
d = Rope diameter (m)
Breaking Torque = (W-S)×Rm
Prepared by Prof. D.B.Patel
Mechanical Engg. Dept
LE. College, Morbi

## Slide 14
Performance Parameters
Friction Power (FP)
Thermal efficiency
Indicated Thermal efficiency
Break Thermal efficiency
Mechanical efficiency
Relative efficiency
Break specific fuel consumption (bsfc)
Mean effective pressure (Pm)
Prepared by Prof. D.B.Patel
Mechanical Engg. Dept
LE. College, Morbi

## Slide 15
Thank You
?